## Slide 1: Validation of the surrogate assisted Bayesian inference equilibrium reconstruction approach on Wendelstein 7-X
R. Köberl, R. Babin, C.G. Albert, K. Rahbarnia and the W7-X Team

## Slide 2: Motivation
forward model
  Equilibrium reconstruction
        Equilibrium reconstruction tries to solve fixed-point problem
        Model and measurements are affected by uncertainty
        Often solved via optimisation
        Evaluation of high-fidelity forward models can be computationally prohibitive
  Goal
      Propagate uncertainties to reconstructed parameters
      Utilise Bayesian formalism
      Data driven methods for faster inference
      Validate on experimental data and compare to established approaches
equilibrium parameters
equilibrium solver
synthetic diagnostics
measured data
inference criterion,
e.g. best fit

## Slide 3: Surrogate assisted Bayesian inference equilibrium reconstruction (surroBIER)
      Create data-base of equilibria and corresponding synthetic diagnostic measurements
      Utilise dimensionality reduction to find low-dimensional representation of equilibria (latent space)
      Approximate the mapping from latent-space to the synthetic diagnostics via surrogate models
      Use latent-space data distribution as prior in Bayesian inference:
Equilibrium data-set
syn. diag. data-set
dim. reduction
latent space
surro. models
measured data
likelihood
surro. models
prior
posterior

## Slide 4: W7-X equilibrium data-set for fixed coil currents
  Sampling equilibrium defining parameters
      radial pressure profile (dim.=7):
  , , kPa
      toroidal current profile (dim.=4):
  ´, , kA
      total toroidal flux (dim.=1):
  Wb
Equilibrium data-set
toroidal flux, principal component analysis truncated at

## Slide 5: W7-X equilibrium data-set for fixed coil currents
  Evaluate VMEC for sampled parameters
      VMEC solution described by more than 80k parameters (Fourier coefficients, iota-points,…)
  Apply dimensionality reduction on VMEC data
      Straight forward and fast method  maintains more than 99% of explained variance
      Linear projection from high dim. space to latent space
      Dimensionality reduction introduces some error
Equilibrium data-set
dim. reduction
latent space
syn. diag. data-set
surro. models

## Slide 6: W7-X equilibrium data-set for fixed coil currents
      Dimensionality reduction introduces some error
Equilibrium data-set
dim. reduction
latent space

## Slide 7: Equilibrium prior
      Create a prior distribution over 12 dim. latent-space representation of equilibria
      Use Bayesian Gaussian mixture model for density estimation (see e.g. here)
Equilibrium data-set
dim. reduction
prior
syn. diag. data-set
surro. models

## Slide 8: Surrogate models for synthetic magnetic diagnostics
Calculate synthetic diagnostic signal from VMEC dataset via DIAGNO
Map latent space representation of VMEC equilibria (principal values ) to synthetic signals
Polynomial regression (PCE) or fully connected feed forward neural-networks
Equilibrium data-set
dim. reduction
prior
syn. diag. data-set
surro. models

## Slide 9: Inference on latent parameters from measurements
measured data
likelihood
surro. models
prior
posterior
likelihood
prior
prior
with
posterior
surro. models
measured data
M
surro. error

## Slide 10: Inference for 20180821.12@5100: latent space
MAP … maximum a posteriori estimation

## Slide 11: Inference for 20180821.12@5100: comparison to high-fidelity model
Compare result to similar STELLOPT optimization with same signals and
          Optimize VMEC free boundary profile (two power), profile (polynomial),
Initialization of VMEC close to surroBIER MAP (boundary, axis, , )
STELLOPT runtime ca. 6h on 7 COBRA nodes, surroBIER MAP few minutes on single laptop core

## Slide 12: Inference for 20180821.12@5100: flux surfaces
low uncertainty on flux surface position
good agreement with STELLOPT
higher uncertainty for the last closed flux surface due to uncertainty in
uncertainty in introduces uncertainty in

## Slide 13: Inference for 20180821.12@5100: iota and pressure-profile
iota-profile directly obtained from re-expansion
pressure-profile calculated from radial force balance
pressure-profile calculated from radial force balance
dim. red. allows for hollow pressure profiles

## Slide 14: Summary
proposed framework for equilibrium reconstruction using dimensionality reduction, surrogate modelling and Bayesian inference: surroBIER
for fixed coil currents allows fast best fit estimate (MAP) and uncertainty quantification via MCMC for flux surfaces, ,
pressure profile can be calculated from radial force balance directly but can be hollow
comparison to high fidelity reconstruction using STELLOPT showed agreement within uncertainty
Future work
improve prior and dimensionality reduction
couple to more diagnostics for better inference on profiles
include more MHD solvers such as GVEC, DESC etc.

## Slide 15: Inference for 20180821.12@5100: rejecting hollow pressure profiles

## Slide 16: Inference for 20180821.12@5100: rejecting hollow pressure profiles

## Slide 17: Other forms of dimensionality reduction: Autoencoder

## Slide 18: Other forms of dimensionality reduction: Autoencoder

## Slide 19: Reconstruction on synthetic validation data