## Slide 1
Jorrit Lion
Max-Planck-Institute for Plasmaphysics Greifwald
Systems Studies of fusion power plants

## Slide 2: Motivation for Fusion Energy
1.5°C goal requires zero global net GHG emissions by 2050 and significant negative emissions after.
Main Share of GHG emissions is in the Energy Sector
DAC requires 300 MW/(MtCO2/yr)
  70 MtCO2/yr (10% of Germany's today's GHG Emissions) requires 21 GW additional power (1/3 of today's electricity production in Germany)
Intermittent renewables require:
  Load Management
  Base-Load
  Storage
  Dispatchable sources
  Transmission Lines
Future demand for GHG emission free power sources, baseload compatible: E.g. Fusion
IPCC, 2021: "Climate Change 2021: The Physical Science Basis."
Noah McQueen et al Prog. Energy 3 (2021)
Platt, John and Pritchard, Orion and Bryant, Drew, Analyzing Energy Technologies and Policies Using DOSCOE, SRNN (2017).
Data: Andrew, Robbie M., & Peters, Glen P. (2021). "The Global Carbon Project's fossil CO2 emissions dataset"
Data
Extrapolation
Target
Energy Consumption Germany
Notes: DAC: Direct Air Capture, DACCS: Direct Air Carbon Capture and Storage

## Slide 3: Fusion – the D-T fuel cycle
D-T cross section 1000 times larger at 10 keV than other fuels
Deuterium and Lithium reserves:
  Deuterium in seawater (0.015%)
  Li Reserves:
    Current on-land reserves: ~30 Mt
    24 EWh/year requires 10 Mt Li for 1000 years
    Li seawater > 200 Gt
    With higher confinement, other burn fuels appear possible (D-He3 e.g.)
D-Li energy density 2 MJ/kg
  (Oil 45 MJ/kg, U-235 8 MJ/kg)
+
+
+
+
D
T
He-4
n
+
+
Li-6
+
T
+
He-4
Plasma
Breeding Blanket
+3.5 MeV
+14.1 MeV
Notes: D extracted by electrolysis of heavy water obtained from freshwater via the GS (Girdler sulfide) isotopic
exchange process

## Slide 4: Fusion – Confinement Concepts
Magnetic confinement
  Tokamak
  Stellarator
  Z-Pinch
  FRC (field – reversed - configurations)
  Spheromak
Inertial confinement
Confined by magnetic fields
Confined by inertia
wikipedia.org/wiki/Field-reversed_configuration

## Slide 5: Stellarators and Tokamaks
Tokamak
Poloidal Field produced by plasma current
Plasma current drive needed
Poloidal field coils
Planar Coils
Pulsed Operation
Stellarator
Poloidal Field produced by coils
No current drive needed
No Poloidal field coils required
Non-planar Coils
Steady State Operation

## Slide 6: Stellarators and Tokamaks: Realised Experiments
Fusion Reactor (???)
LHD (Toki, Japan)
JET (Culham, UK)
W-7X (Greifswald, Germany)
ASDEX Upgrade (Garching, Germany)
ITER (Cadarache, France)
…
under construction
Conceptional Stage

## Slide 7: Extrapolating to a Reactor Plant (on the back of an envelope)
Energy balance:
=1 MW/
=5 MW/
=10 MW/
=2 GW
=1 GW
=500 MW
=6 =95%
=1.4
=7 keV
=1
"High Volume" Fusion
"High Field" Fusion
ignition
Lines of constant
Q=
Q=10
Q=1
Confinement Loss
Bremsstrahlung
Fusion Heating
Aux. Heating
=2 GW
=1 GW
=500 MW
An involved systems problem!

## Slide 8: Fusion Reactor – Key Technological Entities
Coils
  Super-Conductor properties
  Insulation
  Coolant
  Stresses
Blanket
  Neutron Loads
  Tritium Breeding Ratio
First Wall
  Thermal Loads (neutrons, alphas, fast neutrals, gammas)
  Sputtering
Divertor
  Thermal Loads
Support Structure
  Stresses, Ports
Heating
other reactor components (turbines, tritium handling, vacuum pumps,…)
IPP, Karin Hirl

## Slide 9: A systematic way: Systems Codes
Comprehensive models of an entire fusion power plant
Multidisciplinary (physics, engineering, economics)
Fast (design space exploration)
Modular (easily adoptable to new developments)

## Slide 10: A systematic way: Systems Codes - Continued
Iteration Variable: E.g. Major Radius, Magnetic field strength, Temperature, Density…
Objective function: E.g. Cost of electricity, or Capital costs, ..
Inequality Constraints: E.g. Heat flux limits, Neutron Damage, Coil Forces, Quench Protection…
Equality Constraints: E.g. Power output, Q, …
objective function
inequality
equality
Problem: Find saddle point of
Optimization Vector

## Slide 11
Coil related example systems code model

## Slide 12: Technological Constraints in Coils: Critical Current Density
Superconductors require a operating window:
Imposes limits on the magnetic field in the coils
Temperature given by coolant:
  Helium ~ 4 K (or ~2K superfluid)
  Neon ~20 K
  Nitrogen ~70 K
Strain: Bending Strain, depends on conductor size
Magnetic Field
Conductor Strain
Cryogenic Temperature
C. Donelly (2017)
T=4K

## Slide 13: Technological Constraints in Coils: Quench protection
Copper Heat Capacity
Copper el. Resistivity
electrical resistivity [n]
Superconductor
Copper
Coil Quench:
Local heat entry prevents superconductivity
Current flows through copper
Current in resistive copper leads to temperature rise!
Determines minimal amount of copper
Heat deposition
Temperature Rise
Heat capacity and density of copper and coolant (Helium, Nitrogen)
Energy
RRR

## Slide 14: Other constraints in a fusion power plant
U. Fischer, EF Report D1a_2AHVKD (2008)
DEMO
MHD
Heat Exhaust
Forces/Stress
Coil Quench
Strain
Critical current density
Operational Limits
Neoclassic transport
Turbulent transport
Diagnostics
Remote Maintainance
Tritium Breeding
Neutrons (appm, tbr, dpa flux)
Impurities
Helium Ash
…

## Slide 15: Application: HSR-5 – Extrapolating the W7-X line with a systems code
Systems Code: PROCESS
High aspect ratio machine (A=12)
Assumed W7-X like transport
Systems codes models allows finding limiting constraints
ignited HSR5 points (ISS04)
Confinement
Quench Protection
Blanket Requirements
"W7-X" - like
Coil-Plasma distance insufficient
Kovari, M. et al. Fus. Eng. Des. (2014)
Lion, J. et al. Nucl. Fus. (2021)

## Slide 16: Application: Compact QA-Stellarators (Conceptional)
Ignited Reactor configurations, 1.5 GW Fusion power
Assuming W7-X like transport
Cost drivers: Beta limit and Stress
Configuration from: M. Landreman, E. Paul, Phys. Rev. Letters (2022)

## Slide 17: Cost Models
Systems codes typically also include cost models
PROCESS (eurofusion systems code for DEMO):
Largest component in Capital costs are magnets and nuclear technology
COE dominated by deprecation and replaceable components
Disclaimer: Cost models are up for large uncertainties, especially for components and procedures without sufficient experience (e.g. Li-blanket, remote maintenance)
S. Entler et al. "Approximation of the economy of fusion energy", Energy 152 (2018)
Capital Costs
COE

## Slide 18: Summary & Conclusion
Fusion power is a promising candidate for a GHG emission free, long-term power source
Fusion reactor design is a complex, multidisciplinary systems optimization problem
One way to approach this is by utilizing systems codes
  Collection of physics and technological models that reflect all relevant reactor features
  Allows a high level, holistic view of the full power plant
  Can be used to re-iterate with technology and physics optimization
  Allows detailed insights at specific design regions
Systems studies necessary part for analyzing commercialization of fusion energy

## Slide 19
Thank you for your attention!

## Slide 20: Fusion as a potential power supply: Properties
Provide Electricity and/or low and medium temperature Heat (300-700°C)
Baseload power source and/or dispatchable power source
Produces low-level or intermediate-level radioactive waste with no need for final disposal facilities (lifetime ~100 years)
Extensive Fuel reserves > Years
No criticality

## Slide 21: Energy Confinement Scaling Laws
Fusion heating terms need to balance the loss terms
Parametrization in Energy confinement time
  (Exp.) time in which the plasma loses its energy after all heating is turned off
A. Dinklage et al. "Magnetic configuration effects on the Wendelstein 7-X stellarator" Nature Physics 14 (2018)
Thermal Plasma Energy
Energy confinement time
Notes: Lets focus on tokamaks and stellarators where the physics basis is very much explored up to now:

## Slide 22: Technological Constraints: Stress Constraints For High Field Tokamaks
PROCESS: Systems code for tokamaks and stellarators in eurofusion.
In tokamaks magnetic field increase leads to smaller major radius due to improvement of confinement
At higher magnetic field TF coil inboard leg size needs to be increased to cope with increased stresses
Increasing leg size leads to increasing major radius
New ways to cope with stresses at higher fields required
R. Kembleton, M. Siccinio, M. Coleman
increasing stress
higher confinement
Kovari, M. et al. Fus. Eng. Des. (2014)
Lion, J. et al. Nucl. Fus. (2021)

## Slide 23: Now available: HTS
High temperature, high magnetic field cables become commercially available, e.g.:
Fusion Power:
Fusion "Easyness":
Molodyk, A. et al. "Development and large volume production of extremely high current density YBa2Cu3O7 superconducting wires for fusion". Nature Sci Rep 11, 2084 (2021)
Rodriguez-Fernandez, P. et al., "Overview of the SPARC physics basis towards the exploration of burning-plasma regimes in high-field, compact tokamaks". Nucl. Fus. 62, 4 (2022)
Hartwig, Z. S. et al "VIPER: an industrially scalable high-current high-temperature superconductor cable" Supercond. Sci. Technol. 33 (2020)
Commonwealth Fusion Systems (2021): cfs.energy/news-and-media/cfs-commercial-fusion-power-with-hts-magnet