Title page W7-X
w/ EUROfusion acknowledgement
An Engineering based Cost Function for Stellarator coil optimization
Nathan Smith, in collaboration with Felix Warmer, Jorrit Lion and Caoxiang Zhu.
IPP Greifswald
18th March 2022

---
Motivation
- In order for fusion reactors to be commercially successful, they must be economically competitive with other energy sources.
- The most expensive element of any magnetic confinement fusion reactor
  is the magnet system itself.[1]
- Coil size dictated by many factors;
  - Critical current density,
  - Quench protection,
  - Forces and stresses,
  - Coil spacing.
- Project focused on the first such
  constraint, to see if it were possible
  to optimize coils based on it.
[1] S. Entler et al. Energy 152 (2018)
[Speaker Notes: The primary motivation for this project as well as much of modern plasmaphysics and fusion research is to develop Fusion as a viable Baseload energy source for the future. For this to happen however, it needs to be adopted by industry, invested in and bought by consumers. For this commercial success to come about, fusion needs to be economically competitive with other energy sources used today and in the future, such as Renewables, Conventional nuclear and Fossil fuels. One major element of the economics of fusion reactors are the capital costs required to construct them, as they use advanced technology and require large support systems. The most expensive single element of a reactor however is the magnet system itself, in some studies coming to over a third of the total costs of building a reactor. This is because the coils are typically quite large, complex, and made up of superconducting material. The coil size itself is dictated by multiple different factors, namely the critical current density of the superconductor, the requirements for quench protection of the coil, the forces and stresses which are imparted on the coil due to the magnetic fields, and the need to have enough space between coils to allow access for maintenance and other systems. In this project we focused on the first of these constraints, in order to see if it would be possible to optimize coils such that their size, based on the current density, could be minimized.]

---
Content slide w/ W7-X logo
Optimized Reactor Coils
Early stellarator design, SIM-8, 1958
2cd Atoms-For-Peace Conference
- Computational design tools more prevalent than ever.
  - Algorithmic architecture e.g. Vectorworks‘ Marionette.
  - 3D printing of prosphetics, e.g. Sculpteo.
  - Many more, with available computing power
    and data similarly growing.
- Allows stellarator coils to be precisely designed.
- These advances can lead to:
  - Increased productivity,
  - Increased cost effectiveness,
  - Better safety,
  - More flexibility in design.
Increasing
Optimization
[Speaker Notes: Computational methods are becoming more integrated with design techniques with each passing year. Fields such as architecture and prosphetic design already make heavy use of computational methods to maximise the effectiveness of their products while reducing material usage. At the same time as this, computing power and data availability are increasing constantly, allowing these methods to be used faster and with more accuracy than before This has many benefits to the creation of complex machines, such as stellarator fusion reactors, allowing them to be designed by fewer people in a shorter span of time, with greater efficiencies in terms of cost, manufacturing capability and the effectiveness of the product. This is very evident in the design of stellarator type fusion reactors, where the availability of computational tools has allowed the magnetic field coils to be designed with very precise shapes, from which a magnetic field very closely approaching the optimum can be found, and thus maximising the desirable physics properties of the plasmas confined within.]

---
Approach: New cost term for coil volume and forces
- FOCUS: Flexible Optimized Coils Using Space curves[2]
  - Coils in fourier representation in our implementation.
  - Multiple optimizers included, using analytic
    gradients of cost functions.
- Multiple cost functions for coils, which
  usually compete with each other.
  - Bnorm term for field at plasma boundary
  - Coil-surface separation term for desired
    space, e.g. for blanket.
  - Toroidal flux term for field strength.
  - Coil length term to prevent coil snaking.
  - Ect...
[2] Caoxiang Zhu et al 2018 Nucl. Fusion 58 016008
[Speaker Notes: In this talk the optimization code which will be primarily discussed is FOCUS (standing for Flexible optimized coils using space curves). This optimization code represents coils in fourier space, and changes the fourier coefficients of the coils such that the resultant coilset minimzes a cost function. This function is the weighted sum of a set of objective functions, each of which quantify some property of the configuration. For instance, the Bnorm term of the function quantifies the magnetic flux through the plasma boundary across said boundary, and attempts to minimize the absolute value of this. Meanwhile, the Coil-surface separation term is a chi-square term meant to get the average distance between the coil and the plasma boundary as close to a target value as possible.]

---
What’s missing...
- Engineering properties are not considered as much.
  - Coils are treated as 1D filaments of pure current.
  - In reality: Finite 3D superconductors with their specific limits.
  - Can still have a major impact on a reactors design.
  - Important for commercialisation of fusion.
- Coils are an expensive but important part of any design.
  - Wish to reduce cost of raw materials.
  - Need to still meet other requirements.
- Other related coil design challenges:
  - Quench protection, Port access,
    Structural forces, etc.
[Speaker Notes: Although these are extremely useful tools already, they don’t take many of the physical realities of a reactor in to account. These engineering challenges are major elements of actually creating Fusion reactors, but are generally done following the optimisation of the coilset, which itself considers coils as 1D filaments. This means that some designs may be ruled out following optimisation, while others that have good engineering properties aren’t found during the optimisation process due to being almost, but not quite, as good as others. Furthermore, finding designs with good engineering properties is vital to give fusion a good chance at success in a commercial environment, as without these they will take longer to construct, cost more resources and be less effective in many important areas beyond simply confining plasma. One of the most important parts of any magnetic confinement fusion reactor is, obviously, the magnetic coils. However, these tend to be very large, ever more so in fact, are internally complex and made of expensive superconducting material. Because of this, the main focus of the project was to reduce the amount of raw material needed for the coils, while still meeting other constraints on the coil design. Therefore, we needed a tool that could calculate the required size of a coil under a set of operating conditions. Other elements which are affected by the coil shape and sizes are the quench protection, which is very closely tied to the coil sizes, Port access, such that coils have enough separation to give vessel access for fueling, monitoring and maintenance, as well as structural forces, where the support structure of the reactor needs to be capable of handling the forces between the coils.]

---
Method

---
Algorithm for Coil volumes based on current density
Initialise configuration
- Created tool to find coil sizes based on current density.
  - Two main stages:
    - Calculating peak magnetic field
    - Solving current consistency equation.
  - Calculation requires the surface Bfield of finite coils.
  - Lower bound on possible coil size is set by coil
    material properties.
- Computationally expensive task;
  - Requires calculating the field at many points.
  - Previously worked on by J. Lion[3], now
    significantly faster in this implementation.
- Important: Tool can find different size for each coil type.
Calculate Geometry
Calculate peak field strength
Solve for coil size from current constraints
[3] J. Lion et al 2021 Nucl. Fusion 61 126021
[Speaker Notes: In order to produce a cost function that could be used in an optimisation algorithm, we first need a tool that can automatically and quickly calculate the size required, and therefore volume, of a coil. This requires a two stage process of calculating the Magnetic field on the surface of the coil, finding where this field is maximum, and using this information to solve a current consistency equation, shown at the bottom of the chart. Because we need the field on the surface of the coil, the field calculation needs to be made with a method more realistic than a filamentary approximation. For this, we use the method of General cubic elements. Additionally in the second stage, we need to know the material properties of the coils, as these will dictate what the minimum possible size of our coils can be for a certain contained current. This task is rather computationally expensive however, namely in the calculation of Bmax, as this requires finding the field strength on hundreds of points across the coils. Previously this has been worked on by Jorrit, but was not fast enough for use in an optimization algorithm. In this case, we managed to greatly increase the speed of the tool The workflow for the tool is set out on the right, and covers the steps involved in calculating the size of a coil. This process can be done either for a coil set as a whole or for each coil in a set individually, allowing for different coils in a configuration to have different sizes.]

---
General Cubic Element method
- General Cubic Element (GCE) method is used to calculate the
  magnetic field of finite width coils, and thus Bmax
- Coils are approximated as sets of cuboids[4]
  - Elements have analytic solutions for their B field.
  - Field at any point is just the sum of these fields.
- Total field of coilset with i GCE‘s
Bi is the field of element i,
Mi is the transformation to the basis coordinates of i,
ri is the center of the element.
[4] Sackett, S J. EFFI, 1977
[Speaker Notes: As stated before, to calculate Bmax, we need to know the magnetic field of coils of Finite width, rather than filaments. And for this, we use the General Cubic element method. The general cubic element, or GCE, method, is a way of approixmating a coil of finite size as being made up of many small cuboids, as opposed to being a 1D filament in many applications, or as many 1D filaments in other finite size approximations. The former is fine when calculating the field in the plasma region, but for the field close to the coils a better approximation in required. The advantage of this approximation is that the magnetic field of an arbitrary cuboid is known, so can be easily calculated at the point of evaluation for all the elements of a coil. The relavant equation for a single GCE is shown, for a GCE at the origin orientated as shown in the diagram. The full field of a collection of GCE’s is the sum of these fields, rotated and translated appropriately to the positions of their respective element.]

---
Hybrid approach
- GCE calculation computationally expensive
  - Requires 16 calculations of I per GCE, involves logarithms and arctangents. SLOW
  - Filaments only require a single cross product and divisions at each element.
- Use best of both worlds
  - GCE‘s are used for nearby coils.
  - Filaments are used for further coils.
  - The Effect of GCE‘s is negligible
    at long distance.
  - No detriment to accuracy, greatly
    increased speed.
- Increased speed makes calculation feasible within an optimisation algorithm.
[Speaker Notes: The issue with the GCE method is that it is extremely computationally intensive. Each evaluation of the field at a point relative to a GCE requires 16 seperate evaluations of the function I shown in the previous slide, which contains very slow operations involving logarithms arctangents. This must be done for each coil element, when in comparison, filamentary Biot savart only requires a vector product and division by scalar at each element, so is comparatively much faster. To remedy this, coils further away from the evaluation point have their fields calculated using the filamentary method. At these distances, the effects of finite size coils will not be relevant, so the 1D approximation is completely fine. This reduces the number of GCE calculations that must be made significantly while keeping accuracy. Additionally, symmetry arguments can be used to further decrease the number of calculations required. In a W7X configuration, the total field can be calculated by mirroring the field due to one half of a module and adding it to the total, and then rotating this about the torus 5 times. This massive speed up means that the Bmax and subsequently volume can be caculated in very short times, making it feasible for use within an optimisation algorithm.]

---
Maximum B field
- Critical current density of a superconductor drops as local B field increases.
  - Need to calculate minimum critical current density, therefore require
    maximum field strength.
- Calculate this by first finding points on
  inside of the coils.
  - Blue curves are central filaments, colored
    bands are point surfaces.
  - Assume Bmax is always on this surface.
- GCE‘s used for calculation, due to being
  very near coils.
- Find point/points where field magnitude is highest.
  - Find that maxima and near-maxima typically are found
    in areas of high curvature, as shown.
[Speaker Notes: We require Bmax because as the local field strength increases, the critical current density of a superconductor will actually decrease. This means that in order to calculate the minimum critical current density, we need to find the highest field on the coils. In order to find the maximum magnetic field strength on the coils, we make two initial assumptions. Firstly, that the magnetic field across a single module is representative of the field around the whole torus and, secondly, that the field will be at its peak on the inner surface of the coils. With this, we set up grids of points across these inner surfaces, and then use the method presented in the prior slides to calculate the magnetic field at each of these points. We find that the highest magnetic field is typically, although not always, found at areas where coil curvature is high and where coil density is high, with these areas most often being in or near to the helical coil envelope that generates the rotational transform.]

---
Assumptions and error sources in GCE method
[8] S. Babic, C. Akyel, 2005, DOI: 10.1002/jnm.594
- Straight Cuboids: Results in overlap at points of curvature.
  - Overlap exaggerates the calculated field, especially
    near curvature where increased overlap occurs.
  - Could be solved via different element
    geometry, e.g Trapezoids.[8]
- Uniform current density in rectangular winding pack.
  - Current density will change depending on
    winding pack structure and coil shape.
  - Winding pack may not be rectangular in every design,
    for instance, ITER winding pack is a trapezium.
[Speaker Notes: Jcrit Quench protection Forces & stress Spacing Winding pack composition]

---
Superconductor critical current density
- Primary constraint on coil size is current density.
  - Required field on axis sets coil current.
- Plot shows B dependence of critcal
  current of superconductor strands.[5,6,7]
  - T = 4.2 K, negligible strain.
[5] V Braccini et al 2011 Supercond. Sci. Technol. 24 035001
[6] Y Ilyin et al 2007 Supercond. Sci. Technol. 20 186
[7] S B L Chislett-Mcdonald et al 2020 J. Phys.: Conf. Ser. 1559 012063
[Speaker Notes: In order to save on material usage in our reactors, we wish to make the cross sectional size of our coils as small as possible, in order to reduce the overall volume and therefore mass. However, this can only be done up to a certain point due to material properties of the super conductor. The primary constraint of this nature is the current within the coil. In order to achieve a certain magnetic field strength on axis, the required currents in the coils are fixed, for fixed geometry. Therefore, the current density within the superconductor will be proportional to the inverse square of the coils width. One property of superconductors however is that the current density can only be so high before the material stops being superconducting, so should the current density exceed this, the coil could suffer quenching. Addtionally, The value of this critical current is dependent on the magnetic field acting upon the coil, decreasing as the applied field increases. This leads to a situation where decreasing the coil size results in a higher current density within the coil, while the maximum surface B field increases, resulting in the critcal density dropping. The plot of the right shows the variation of critical current with magnetic field in various super conducting materials held at 4.2 Kelvin. The critical current is also functions of temperature and strain, however in our studies we assumed a constant temperature of 4.2 K and negligible strain, as this as a small effect comparatively.]

---
Solving for coil size
- Use this Information to set up a consistency condition.
  - : Width in direction I.
  - : fraction of material m in
    coil.
  - : safety factor, proportion of
    critical current in coil.
  - : critical current function.
- Can be solved numerically.
  - Vary width to find new field strength
    at the max point.
  - Find width value, i.e. the root of the consistency equation,
    via Newton-Raphson method.
[Speaker Notes: Now that we know the required current within the coil, the maximum Bfield on the coils surface at some arbitrary size, and the variation of the critical current with magnetic field for our chosen material, we can set up our consistency condition for the coil. Taking in to account that only a fraction of the coil will be made up of superconductor after accounting for copper, coolant and structural material, and that for safety reasons we will only wish for our coil to be at a certain proportion of the allowable current density, it is trivial to say that the coil current is equal to the critical current density, multiplied by the cross sectional area and fractions stated above. We can then solve the equation by varying the coil width and calculating the resultant value for Bmax, then via the newton-raphson method, iterate this until the solving width is found. With the width, we can find the cross sectional area of the coil and from this the total coil volume.]

---
Assumptions and error sources
- Critical current functions are parameterized based on
  empirical measurements.
  - Could contain errors or be inaccurate in some regimes,
    for instance the functions diverge close to zero B field.
  - Assumes a constant temperature for the entire coilset.
- Negligible strain in conductor.
  - Will be dependent on the internal forces and shape of the coil.
  - Strain can effect critical current density functions, affecting
    real volume calculation.
  - REBCO based HTS tapes are especially strain dependent.
- Coil composition can be freely set, possibly not being accurate to actual structure.
  - Additionally assumes homgenous internal structure, not necessarily correct.
[Speaker Notes: Jcrit Quench protection Forces & stress Spacing Winding pack composition]

---
Full Algorithm overview
- The coil data is initialised
  - Interpolate coil points for equal spacing, to minimize overlap errors.
  - Scale currents in coils to achieve desired field on-axis.
  - Find configuration symmetries.
- Coil geometry is calculated
  - Basis vectors and GCE sizes calculated.
  - Find points on coil surfaces.
- Calculate Maximum field strength.
- Iteratively calculate coil width.
  - Shift max point to match change in width
  - Calculate new Bmax, resulting jc, and
    result of consistency equation, iterating
    towards root of equation.
[Speaker Notes: We can now layout the full process of the tool. Before doing anything, the data making up the coil data must be checked. The points defining the points along the coil filaments are interpolated such that they are approximately equally space across the coil, otherwise there will be increased overlap between GCE’s at some points, resulting too high fields at these points. The currents in the coils are also scaled in order to achieve the desired on-axis field for the configuration. The number of field periods, coil types and whether the modules are symmetric is also found if this is not already known. The coil data for a group of coil types is then given to the calculation tool, which calculates the geometric elements of the configuration at the given width, namely the basis vectors defining the orientation of the cuboid elements and the dimensions that such elements have. Using this, a grid of points on the inside of the coil surfaces is found and the fields at such points calculated. This is done using GCE’s for the coil on which they rest, and filaments for all other coils, in order to decrease the computation time. The point where the magnitude of these fields is highest is then found. Using this and the reactor parameters which we know such as coil composition and coolant temperature, the consistency equation is set up as shown on the previous slide. The width of the coil is then varied, similarly to as shown in the image. The maximum point is shifted by the change in width in the direction of the local x basis vector, and the new value of the field calculated. This can be then used to calculate the new critical current in the coil, and as such whether the width still satisfies the consistency condition. This is done iteratively until the equation is solved and we have found the optimum size of the coils for this condition.]

---
Benchmarks

---
Accuracy testing
- Field calculation accuracy tested with an Ideal torus of circular coils.
  - 5 m Major radius, 1 m Minor radius
  - 100 Coils, 1 MA each.
  - Found that within torus ‘bulk’, the field matched
    the expected variation from Ampere’s law.
  - From 4.1 m to 5.9 m, reduced χ² = 0.00092,
    for coils with width 5 cm.
- Additionally calculated coil size required to
  reach specified maximum on-coil field.
  - Calculated a winding pack cross section of
    16.3 cm x 22.2 cm for a maximum of 6.18 T
    on-coil with 3 T on-axis.
[Speaker Notes: Jcrit Quench protection Forces & stress Spacing Winding pack composition]

---
Benchmarking
- Improved on prior algorithms which perform similar tasks
  - Previous implementations of the 200 coilset calculation took up to an hour.
  - Only capable of calculating single width for each coil set.
  - With new implementation, calculation for all 200 coilsets takes <1 minute.
  - Can also find independent sizes for each coil type.
- Acheived this through variety of methods;
  - Rewrote field calculation code in compiled format: C++ extension for python.
  - Removed unnecessary calculations, e.g. GCE method for distant coils.
  - Removed overhead in method for repeated calculation, e.g. Basis vectors.
  - Implemented multithreaded calculation of many points.
[Speaker Notes: The information covered here, as stated before, has already been implemented to calculate coil volumes in the past, namely by Jorrit in his PrePROCESS code. However, these implementations are comparatively slow and almost certainly wouldn’t be suitable for an optimisation algorithm due to this. Additionally, the slow speed meant that these implementations could only be used for configurations with the same coil size for every coil. In the new implementation, the tool is significantly quicker, capable of finding a volume for every single configuration in the previously shown database in less than a minute. Additionally, the saved time means that it is effective to find the result for multiple different coil sizes for different coil types. This is very useful in situations such as the W7X planar coils, the various different coil types in tokamaks and the LHD, and optimised stellarator designs where coil shape, size and density varies greatly across a module. This speed up of the methods has been achieved using a variety of methods. The main speed ups have come from rewriting the implementation in C++, in order to take advantage of it being a compiled language and its better memory management solutions than python, and by making use of the Hybrid field calculation mentioned previously. As the effect of finite coils isn’t seen at large distances from coils, there is little to no loss in accuracy by only using the GCE method for the very closest or closest few coils. By replacing the field calculation for the remaining coils with filamentary Biot-savart, which is orders of magnitude faster than the GCE method, calculation times are reduced to nearly the fraction of coils used with GCE’s compared to the original time. Additionally, overhead for many calculations, for instance calculation of the coil basis vectors and GCE sizes, is reduced in newer implementations, so that for a single coil set the basis vectors only need to be calculated once if no coils are changed. Finally, the ability to use multiple threads in the calculation is implemented, to make use of more modern CPU architectures.]

---
Results

---
Width calculation examples
Ability to calculate sizes for each coil type individually allows for tool to be used with many types of coilsets.
Example Heliotron
Two toroidal helical coils,
Six poloidal coils.
Helical coil width: 22.5 cm
On-axis field: 3 T
Major Radius: 3.5 m
Poloidal coil widths: 4.4 cm, 12.7 cm, 14.9 cm
Bmax = 8.85 T
QH stellarator
Four Modules
13 coils per module
Coil sizes varying from
0.6 cm to 2.9 cm.
Major radius ~2 m
Current per coil: 0.1 MA
Bmax = 0.72 T
Miniature Stellarator.
Two outer coils, radius 1.08 m.
Two interlocking inner coils,
radius 0.41 m.
Using REBCO instead of copper, produces 1 T on axis.
Bmax = 5.29 T
[Speaker Notes: Here we can see the tool implemented in a few coil sets whose geometries require that the coils have significantly different coil shapes. On the right is a FOCUS optimised stellarator design. In this design there are 4 modules with a sinusoidal shaped axis, arranged in a square shape. The distribution of currents varies across the module, resulting in coils closer to the end of each module needing to be larger, while the central coils can be much thinner, saving on overall coil volume and preventing coil clashes between the more closely packed coils in the middle. In the middle coil set, we can see the Large Helical Device stellarator, with its 2 Helical coils around the torus and poloidal coils surrounding these. Once again, we can see the differing coil sizes resulting from the differences in coil position, geometry and current. Finally there is the CNT, a miniture stellarator design originally made with copper to produce low fields. It can be seen though that it can produce much higher fields on axis however when using HTS tape based coils at 4.2K. This is not possible with materials such as NbTi or NB3Sn, which produce large coil clashes.]

---
Results for W7X
- Tested the tool using 200 W7X-like designs generated by J. Lion with FOCUS.
  - Same plasma boundary and field strength on-axis.
  - Differing numbers of coils, initial coil radii, and coil length weights.
  - More coils = less total coil!
  - Increased current per coil→ Increased current density & Bmax
    → Coil must be larger to not exceed critical current density.
Six coils, initial radius 1.1 m
Twelve coils, initial radius 1.1 m
[Speaker Notes: Using this tool, we computed the total volumes of a database of 200 W7X like coil sets. The sets have all been produced using the FOCUS algorithm. Each had differing numbers of coils, Different initial radii for the starting coils, and different weightings on the complexity cost function within FOCUS. The Results of these runs for a single coil width for each coil set are shown in these plots. One shows computations with coils made up using Niobium-Titanium super conducting strands, while the other shows results when used Niobium-Tin instead [Maybe use REBCO instead?]. An interesting result of this test is that the volume actually decreases as you increase the number of coils. This is because for less coils, in order to achieve the required field on axis the current contained within each coil needs to be increased. For the same coil width between 2 configurations, this not only means that the current density within the configuration with less coils is higher, but the peak magnetic field strength on the surface of those coils is higher, decreasing the maximum allowable current density. This results in the width of the coils needing to be much larger, with the cross sectional area and volume therefore increasing by a factor of the square of the ratio of the width change. The diagrams on the right showcase this for 2 coil sets which have the primary difference of coil number. The coils on the 6 coil module have to be much larger than the coils on the 12 coil module in order to remain superconducting.]

---
Testing different materials
- The tool can be used to analyse various elements of coilsets made up of different material types.
  - Here, we tested the W7X configuration twice; once using NbTi coils, and again with REBCO, to test how the results differ.
  - Both cases: 3 T on axis, 4.2 K coil temperature, 5 % SC fraction, 80% safety factor.
NbTi Coils
Bmax on coil: 8.03 T
Toroidal width: 10.55 cm
Radial width: 12.87 cm
Total volume: 5.78 m³
REBCO Coils
Bmax on coil: 9.02 T
Toroidal width: 8.14 cm
Radial width: 9.93 cm
Total volume: 3.44 m³
[Speaker Notes: Using this tool, we computed the total volumes of a database of 200 W7X like coil sets. The sets have all been produced using the FOCUS algorithm. Each had differing numbers of coils, Different initial radii for the starting coils, and different weightings on the complexity cost function within FOCUS. The Results of these runs for a single coil width for each coil set are shown in these plots. One shows computations with coils made up using Niobium-Titanium super conducting strands, while the other shows results when used Niobium-Tin instead [Maybe use REBCO instead?]. An interesting result of this test is that the volume actually decreases as you increase the number of coils. This is because for less coils, in order to achieve the required field on axis the current contained within each coil needs to be increased. For the same coil width between 2 configurations, this not only means that the current density within the configuration with less coils is higher, but the peak magnetic field strength on the surface of those coils is higher, decreasing the maximum allowable current density. This results in the width of the coils needing to be much larger, with the cross sectional area and volume therefore increasing by a factor of the square of the ratio of the width change. The diagrams on the right showcase this for 2 coil sets which have the primary difference of coil number. The coils on the 6 coil module have to be much larger than the coils on the 12 coil module in order to remain superconducting.]

---
Application &
Further work

---
Integration with FOCUS
- Began working with C. Zhu to include tool as part of coil optimisation code, FOCUS
  - FOCUS is a Fortran based code, performs optimisation internally.
  - Can be used through a Python interface, tool must be included via this.
- Minimizes maximum field strength rather than volume.
  - Size, therefore volume, directly related to Bmax.
  - Less computation needed for only Bmax.
- Bmax gradient calculated via Forward Finite Differences.
  - FOCUS uses analytic derivatives, Bmax analytic derivative needs further work.
  - With five coil types & six Fourier harmonics, a configuration has 195 DoF‘s
    → Lots of calculations needed for gradient!
- Currently work on this is still in progress, requires more investigation on cost function‘s behaviour.
[Speaker Notes: With a completed tool that can accurately determine the volume of a coil, we began to work on integrating it with the optimization tool FOCUS. Due to the nature of FOCUS, the tool has to be added externally, making the main optimisation algorithm done via scipy instead of FOCUS’s built-in solvers. The overall method used for the original cost function is the same. In order to further increase computation speed, rather than calculating the entire volume of the coils at an iteration step, only the peak magnetic field strength is calculated and minimized. We chose this as the required size will be directly related to the maximum B field, and parameters such as coil number and initial radius will not be modified during optimization. The gradient of the maximum magnetic field is calculated using forward finite differences. This is in opposition to the analytic derivatives used by other FOCUS cost functions, as such a derivative hasn’t been fully worked out yet. FD step size is varied based on the respective parameter. For a 5 coil type stellarator with fixed currents in coils parameterised by 6 fourier harmonics, there are 195 independent degrees of freedom. Because of this, without the increased speed of the calculation, integrating a cost function based on former implementations of the tool would not be feasible.]

---
Possible extensions
- Include other aspects of engineering properties
  - Quench protection, many aspects involved in volume calculation influence this.
  - Port access, finite sized coils will reduce available area.
  - Structural support, forces calculation for superconductor stress
    and support structure stress.
- Further develop material package
  - Include more materials, e.g. Copper, specific HTS composites.
  - Allow coils to use combinations of materials
  - Allow for different materials on different coils in the same configuration.
  - Include other material parameters, e.g. structurally relevant properties such as stress/strain.
  - Include strain effects on superconductor critical current, especially important for HTS.
[Speaker Notes: From here, there are multiple directions that work in this area could be taken. Firstly, more engineering aspects of a fusion reactor could be accounted for. Factors such as required quench protection, availability of space around the torus for ports, and required structural support for the coils could be evaluated and given their own cost functions to use in FOCUS or some other coil code or a systems code. A more comprehensive materials system could be included. Currently the package only includes NbTi, Nb3Sn and a generalised REBCO-type material. One of these can only be used throughout the reactor. Improvements could be made by allowing different coils to be made up of different materials or combinations of materials, as well as including more materials such as copper and specific HTS composites, with other important material functions such as structurally relevant models.]

---
Summary
- We further developed existing models with GCE’s to create a fast tool to calculate coil volumes based on critical current constraints.
- The produced tool can quickly return a coilsets maximum field strength,
  volume, various coil sizes.
- Can be used to quickly investigate different operating temperatures, materials, coil compositions, ect.
- Began integrating with FOCUS, a coil optimization code, to investigate effects of volume-based optimization on coil design, still requires work.
- Further work needs to be done on including more engineering considerations and making the model more detailed.
Thank you!
Source code and additional Documentation can be found at
https://gitlab.mpcdf.mpg.de/fwa/coil_cost_function
[Speaker Notes: So in summary, making use of computationally optimized coils is important for stellarator development, but current and future codes need to include engineering considerations to better match plans for commercialization of fusion. In this project we took existing models and methods used to calculate the minimum required winding pack size of superconducting coils, and streamlined and improved them to be not only more flexible but such that they could be used in optimization codes for coils, such as FOCUS. This produced an easy to use tool that can calculate the sizes required for many possible coil sets very quickly, as well as finding multiple different coil sizes for other types of magnetic confinement systems such as tokamaks. Additionally, we began integrating this tool with FOCUS, in order to try and investigate if doing so would result in novel or significant design changes in the coil sets produced by such coils. We also included the capability to make these investigations under different material considerations, such as those when using REBCO based coils. More work can be done on including the tool in optimization codes, and further features could be included with the methodlogy in order to account for other engineering elements of fusion reactor design.]