## Slide 1: Investigation of fast ion wall loads in W7-X by IR thermography.
Coffee talk IPP 22nd of April 2022
Master Internship
Mark J.H. Cornelissen
Supervisors: Samuel Lazerson (IPP), Josefine Proll (TU/e)

## Slide 2: Fast ions can damage plasma-facing components
Fast ion wall loads in W7-X
[1] S.Äkäslompolo et al. Fusion Eng. Des 146 (2019) 862-865
[1]
D-T reaction generates fast ions.
Fast ion loads limit fusion devices.
Loads concentrate at ‘hot spots’.
To apply mitigation strategies, fast ion models are required.
Verification of models by experiments.

## Slide 3: Research Question: What are the magnitude and location of fast ion wall loads in W7-X?
Compare experimental results to numerical simulations.
Basis for the verification of fast ion models.
Fast ion wall loads in W7-X

## Slide 4
[2]
In W7-X, the fusion alphas are mimicked by NBI.
Two neutral beams inject neutral hydrogen.
Energy (55 keV) of neutral
hydrogen chosen such that their
confinement is selfsame to
fusion alphas.
[2] S.Äkäslompolo et al. Nucl. Fusion 58 (2018) 082010
Fast ion wall loads in W7-X
NBI particles mimic fusion alphas

## Slide 5: W7-X has a five-fold toroidal symmetry
Each toroidal segment has an upper and lower divertor module.
NBI injects neutrals into toroidal module 2.
Each divertor module is
monitored by an IR camera.
Fast ion wall loads in W7-X

## Slide 6: The infrared cameras monitor each divertor
Horizontal Divertor:
[1] Low-iota target
[2] Middle target
[3] High-iota target
[4] Vertical divertor
[5] Baffle plates
[6] AEF port
Fast ion wall loads in W7-X

## Slide 7: Fast ion loads depend on mag. configuration
Discharges with different
magnetic configurations:
Standard configuration;
High-mirror configuration;
High-iota configuration.
ECRH start-up followed by NBI operation phase.
During NBI operation, and are altered.
Fast ion wall loads in W7-X

## Slide 8: 1D heat model is applied to obtain heat flux
The following assumptions are made:
Semi-infinite solid.
Cooling effects are negligible.
Diffusion of heat is negligible along the surface.
1D transient heat conduction model can be applied to obtain the heat flux:
where
Fast ion wall loads in W7-X

## Slide 9: Strike line is monitored to verify method
Standard configuration
Standard: 20180919.33
Fast ion wall loads in W7-X

## Slide 10: Strike line is monitored to verify method
Standard configuration
Temperature shows square root dependence on time.
Fit is obtained with
acceptable uncertainties.
Change in plasma parameters does not significantly alter the heat flux.
Standard: 20180919.33
Fast ion wall loads in W7-X

## Slide 11: Method and THEODOR show good agreement
THEODOR
Method
Only small discrepancies in the tail of the strike line.
The magnitude differs on average 5%.
High-iota configuration
High-iota: 20180822.12
2D heat diffusion equation:
Fast ion wall loads in W7-X

## Slide 12: Fast ion wall loads are positioned at baffle
No loads present
during ECRH startup phase.
Fast ion loads are present
during NBI operation.
Load due to fast ions
trapped in magnetic ripples.
Standard configuration: 20180919.16
Fast ion wall loads in W7-X

## Slide 13: Magnetic configuration alters heat deposition
Standard configuration
20180919.20
High-mirror configuration
20181009.43
Fast ion wall loads in W7-X

## Slide 14: Method to obtain the fast ion heat flux
High-mirror configuration
High-mirror: 20181009.43
Fast ion wall loads in W7-X

## Slide 15: Asymmetries are present in the fast ion loads
Fast ion loads are only present in
the upper sections of W7-X.
Up-down asymmetry:
attributed to drifts.
Toroidal asymmetry:
attributed to solely neutral injection
into toroidal module 2.
Fast ion wall loads in W7-X

## Slide 16: Baffle loads due to trapped particle orbit
Fast ion wall loads in W7-X
Magnetic mirrors due to toroidal variation in magnetic field strength.
Magnetic well between toroidal module 2 and 3 is most populated by NBI.

## Slide 17: Fast ion load is dependent on plasma density
More pronounced toroidal
asymmetry with increasing density.
Fast ion wall loads in W7-X
High-mirror configuration Discharge: | Toroidal asymmetry factor
20180823.28 | 
20180823.39 | 
20180823.37 | 
20181009.43 | 
High-mirror configuration Discharge: | Toroidal asymmetry factor
20180823.28 | 
20180823.39 | 
20180823.37 | 
20181009.43 | 

## Slide 18: Competing effects of density on fast ion loads
Shine-through of NBI decreases
with increasing density.
Birth profile becomes more
core peaked with increasing density.
Collisional effects become more
pronounced with increasing density.
Fast ion wall loads in W7-X

## Slide 19: The results are compared to simulations
Simulations of fast ion trajectory
BEAMS3D gyro-center code
ASCOT full orbit code
Agreement in up-down asymmetry.
Toroidal asymmetry and magnitude
are not yet well predicted.
Fast ion wall loads in W7-X
High mirror configuration Upper section | Fast ion heat flux (kW/) | 
Toroidal module: | Simulation | Experiment
Module 1 |  | 
Module 2 |  | 
Module 3 |  | 
Module 4 |  | 
Module 5 |  | 
High mirror configuration Upper section |  | 
Toroidal module: | Simulation | Experiment
Module 1 |  | 
Module 2 |  | 
Module 3 |  | 
Module 4 |  | 
Module 5 |  | 

## Slide 20: Conclusion
Evidence of fast ion loads on the baffle plates next to the AEF ports.
Up-down asymmetry due to magnetic curvature drifts.
Toroidal asymmetry due to solely injection of neutrals into module 2.
Qualitative agreement in up-down asymmetry between experiments and simulations, but magnitude and toroidal asymmetry are not yet well predicted by simulations.
Fast ion wall loads in W7-X

## Slide 21: Outlook: fast ion loads on the divertor
During NBI operation, the divertor obtains both
convective loads from the thermal plasma particles
fast ion loads from highly energetic particles
Mimic NBI heating system with ECRH heating to assess the fast ion wall loads on the divertor in the upcoming campaign of W7-X.
Fast ion wall loads in W7-X

## Slide 22: Second strike line is formed at high-iota target
Second strike is already
visible during solely
ECRH operation.
Heat distribution changes
drastically when NBI fires.
Difficult to disentangle
convective loads and fast
ion loads.
High-iota: 20180822.022
Fast ion wall loads in W7-X

## Slide 23: Method to obtain the anomalous loads
High-iota configuration
High-iota: 20180822.012
Fast ion wall loads in W7-X

## Slide 24: Origin of the anomalous loads
The convective loads redistribute
due to changing plasma parameters.
Toroidal and up-down asymmetry
suggest that the fast ions do
play a role.
Fast ion wall loads in W7-X

## Slide 25: Conclusion
Anomalous loads are found at the high iota part of the divertor target.
The convective loads redistribute during the NBI operation due to changing plasma parameters.
The asymmetries suggest that the fast ions do play a role.
Fast ion wall loads in W7-X

## Slide 26: W7-X has toroidal variation in magnetic field
The bean-shaped cross-sections are positioned in the middle of each toroidal segment and have the highest magnetic field ()
Fast ion wall loads in W7-X

## Slide 27: Fast ion loads depend on mag. configuration
The rotational transform is the inverse of the safety factor and is given by
where, is the poloidal magnetic flux, and is the toroidal magnetic flux.
The mirror ratio is defined as
Determines the toroidal variation in the magnetic field.
Fast ion wall loads in W7-X

## Slide 28: Fast ion loads depend on mag. configuration
Standard configuration (, )
High-mirror configuration (, )
High-iota configuration (, )
Fast ion wall loads in W7-X
[3] S.Äkäslompolo et al. Fusion Eng. Des 146 (2019) 862-865
[3]

## Slide 29: View of the IR camera
[1] Low iota divertor target
[2] Middle divertor target
[3] High iota divertor target
[4] Vertical divertor target
[5] Pumping gap
[6] Baffle
[7] Outer vessel wall (steel)
[8] Shield (graphite)
[9] AEA port
[10] AEF port
20180823.039
Fast ion wall loads in W7-X

## Slide 30: Discharges
Fast ion wall loads in W7-X

## Slide 31: Temperature dependence of material properties
Change in surface temperature:
, where
.
Fitted to polynomial:
,
where and are fitting
parameters.
Fast ion wall loads in W7-X

## Slide 32: Verification with THEODOR
Discrepancies in magnitude of on average 5%, deemed acceptable.
Fast ion wall loads in W7-X

## Slide 33: Second strike line (High iota configuration)
ECRH operation
ECRH + NBI operation
Fast ion wall loads in W7-X
AEF40, High iota configuration: 20180822.22

## Slide 34: Second strike line (High iota configuraiton)
ECRH operation
ECR + NBI operation
AEF11, High iota configuration: 20180822.22
Fast ion wall loads in W7-X

## Slide 35: Second strike line (Standard configuration)
Standard configuration 20180919.016
ECRH
ECRH+NBI
Fast ion wall loads in W7-X

## Slide 36: Second strike line (Standard configuration)
ECRH
ECRH+NBI
Fast ion wall loads in W7-X
Standard configuration 20180919.016