## Slide 1: Influence of plasma parameters on sawtooth instabilities at W7-X
Written and presented by Tilly Smith
Supervision: Prof. Robert Wolf, Dr. Marco Zanini

## Slide 2: Motivation
Continuation into research of unexpected sawtooth instabilities at W7-X

## Slide 3: Motivation
Continuation into research of unexpected sawtooth instabilities at W7-X
Gain better understanding of when and how instabilities occur

## Slide 4: Motivation
Continuation into research of unexpected sawtooth instabilities at W7-X
Gain better understanding of when and how instabilities occur
Control of sawtooth instabilities is twofold:
  Minimize effect on overall plasma performance
  For instance make use of sawtooth instabilities for impurity control of the plasma

## Slide 5: Motivation
Continuation into research of unexpected sawtooth instabilities at W7-X
Gain better understanding of when and how instabilities occur
Control of sawtooth instabilities is twofold:
  Minimize effect on overall plasma performance
  For instance make use of sawtooth instabilities for impurity control of the plasma
Specifically: examination of the crash interval Δt with respect to other plasma parameters

## Slide 6: Introduction
Crash of plasma electron temperature Te coincides with electron cyclotron current drive (ECCD) experiments
20171206.025
M. Zanini

## Slide 7: Introduction
Crash of plasma electron temperature Te coincides with electron cyclotron current drive (ECCD) experiments
20171206.025
M. Zanini
M. Zanini
20171206.025

## Slide 8: Introduction
Crash of plasma electron temperature Te coincides with electron cyclotron current drive (ECCD) experiments
Strong and repetitive crashes (up to 65% of Te)
20171206.025
M. Zanini
M. Zanini
20171206.025

## Slide 9: Introduction
Crash of plasma electron temperature Te coincides with electron cyclotron current drive (ECCD) experiments
20171206.025
Strong and repetitive crashes (up to 65% of Te)
Diamagnetic energy Wdia and toroidal current Itor affected
20171206.025
M. Zanini
M. Zanini

## Slide 10: Introduction
M. Zanini
ECE central channel temperature profile:

## Slide 11: Introduction
Crash amplitude ΔTe: relative electron temperature change in percent
Inversion radius rinv: radial position where Te=const. before and after a crash
M. Zanini
ECE central channel temperature profile:

## Slide 12: Introduction
M. Zanini
Iota-profile:

## Slide 13: Introduction
Temporal evolution of iota-profile (1d cylindrical system):
M. Zanini
Iota-profile:

## Slide 14: Introduction
Temporal evolution of iota-profile (1d cylindrical system):
Dimensional analysis results in the resistive time:
M. Zanini
Iota-profile:

## Slide 15: Introduction
Temporal evolution of iota-profile (1d cylindrical system):
Dimensional analysis results in the resistive time:
assuming L2~rinv2:
M. Zanini
Iota-profile:

## Slide 16: Introduction
Temporal evolution of iota-profile (1d cylindrical system):
Dimensional analysis results in the resistive time:
assuming L2~rinv2:
→ hypothesis: τR~Δt
M. Zanini
Iota-profile:

## Slide 17: Plotting Δt over rinv/a
Linear fit in logarithmic scale: y = a + x∙b
Residuals in logarithmic scale
Power fit and residuals in linear scale

## Slide 18: Plotting Δt over rinv/a
Linear fit in logarithmic scale: y = a + x∙b
Histogram of residuals resembles a Gaussian distribution
Residuals in logarithmic scale
Power fit and residuals in linear scale

## Slide 19: Plotting Δt over rinv/a – all discharges
Improve statistic by plotting all discharges together

## Slide 20: Plotting Δt over rinv/a – all discharges
Improve statistic by plotting all discharges together

## Slide 21: Results Δt over rinv
Coefficient of determination: ϵ[0,1]
  Observed quantity
  Predicted value
  Mean value

## Slide 22: Results Δt over rinv
Coefficient of determination: ϵ[0,1]
  Observed quantity
  Predicted value
  Mean value
data sets small, error margins large
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 23: Results Δt over rinv
Coefficient of determination: ϵ[0,1]
  Observed quantity
  Predicted value
  Mean value
data sets small, error margins large
Fit parameters (y = a + x∙b) and R2 for all discharges:
Average exponent: b = 3.12±0.98
→ hidden rinv dependency to decrease discrepancy?

## Slide 24: Plotting η-1 over rinv/a
What other parameters influence τR?

## Slide 25: Plotting η-1 over rinv/a
What other parameters influence τR?
Spitzer plasma resistivity:

## Slide 26: Plotting η-1 over rinv/a
What other parameters influence τR?
Spitzer plasma resistivity:
  Coulomb logarithm ln(Λ)=17
  Effective atomic number deemed to be Zeff=2.5
  Electron temperature estimated at the inversion radius:
  Central electron temperature Te,0

## Slide 27: Plotting η-1 over rinv/a
What other parameters influence τR?
Spitzer plasma resistivity:
  Coulomb logarithm ln(Λ)=17
  Effective atomic number deemed to be Zeff=2.5
  Electron temperature estimated at the inversion radius:
  Central electron temperature Te,0
→ what dependency does η have on rinv?

## Slide 28: Results η-1 over rinv/a
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 29: Results η-1 over rinv/a
Average exponent: b = -2.18±0.83
  Opposite of necessary trend to decrease discrepancy
→ scaling method or hypothesis insufficient?
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 30: Results η-1 over rinv/a
Average exponent: b = -2.18±0.83
  Opposite of necessary trend to decrease discrepancy
→ scaling method or hypothesis insufficient?
Further scaling methods are performed
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 31: Plotting Δt over τR,inv
Aim is to obtain a “local” resistive time at rinv
  Calculate with previously introduced η

## Slide 32: Plotting Δt over τR,inv
Aim is to obtain a “local” resistive time at rinv
  Calculate with previously introduced η
Large scattering in linear and logarithmic scale

## Slide 33: Plotting Δt over τR,inv
Aim is to obtain a “local” resistive time at rinv
  Calculate with previously introduced η
Two Gaussian distributions can be identified
Large scattering in linear and logarithmic scale

## Slide 34: Plotting Δt over τR,inv
Aim is to obtain a “local” resistive time at rinv
  Calculate with previously introduced η
Two Gaussian distributions can be identified
Large scattering in linear and logarithmic scale
→ where do the cluster formations come from?

## Slide 35: Plotting Δt over τR,Zsingle and τR,Zavg
Variation for Zeff value in τR,inv :
  Using individual values Zsingle for each crash
  Using an average value

## Slide 36: Plotting Δt over τR,Zsingle and τR,Zavg
τR,Zavg shows no
reliable dependency
Variation for Zeff value in τR,inv :
  Using individual values Zsingle for each crash
  Using an average value
τR,Zsingle still has
cluster formations

## Slide 37: Results Δt over τR,inv
R2 for all discharges:

## Slide 38: Results Δt over τR,inv
R2 for all discharges:
Zeff value has an effect on the data, but:
  τR,Zsingle and τR,Zavg improve goodness in individual discharges

## Slide 39: Results Δt over τR,inv
R2 for all discharges:
Zeff value has an effect on the data, but:
  τR,Zsingle and τR,Zavg improve goodness in individual discharges; overall
  unreliable scaling methods

## Slide 40: Results Δt over τR,inv
Fit parameters (y = a + x∙b) for all discharges:
Negative exponent unexpected, no explanation found
R2 for all discharges:
Zeff value has an effect on the data, but:
  τR,Zsingle and τR,Zavg improve goodness in individual discharges; overall
  unreliable scaling methods

## Slide 41: Results Δt over τR,inv
Negative exponent unexpected, no explanation found
R2 for all discharges:
Zeff value has an effect on the data, but:
  τR,Zsingle and τR,Zavg improve goodness in individual discharges; overall
  unreliable scaling methods
Average exponent: b = 2.73±0.79
  Deviates from expected exponent of 1
Fit parameters (y = a + x∙b) for all discharges:

## Slide 42: Plotting Δt over <τR>
Aim is to mitigate fluctuations of individual quantities throughout the instability region

## Slide 43: Plotting Δt over <τR>
Aim is to mitigate fluctuations of individual quantities throughout the instability region
Effective resistive time:

## Slide 44: Plotting Δt over <τR>
Aim is to mitigate fluctuations of individual quantities throughout the instability region
Effective resistive time:
  Integrated over instability volume
  Using the effective electron temperature:

## Slide 45: Plotting Δt over <τR> - all discharges

## Slide 46: Plotting Δt over <τR> - all discharges
Cluster formations can be identified

## Slide 47: Results Δt over <τR>
Variations in Zeff values:
  Has an influence on data
  Only influence causing the scattering?

## Slide 48: Results Δt over <τR>
Fit parameters (y = a + x∙b) for all discharges:
Negative exponent unexpected, no explanation found
Variations in Zeff values:
  Has an influence on data
  Only influence causing the scattering?

## Slide 49: Results Δt over <τR>
Average exponent: b = 1.07±1.15
  Percentage error of >100%
Negative exponent unexpected, no explanation found
Fit parameters (y = a + x∙b) for all discharges:
Variations in Zeff values:
  Has an influence on data
  Only influence causing the scattering?

## Slide 50: Results Δt over <τR>
Variations in Zeff values:
  Has an influence on data
  Only influence causing the scattering?
Average exponent: b = 1.07±1.15
  Percentage error of >100%
  → unreliable results
Negative exponent unexpected, no explanation found
Fit parameters (y = a + x∙b) for all discharges:

## Slide 51: Plotting Δt over η-1
Is the assumption L2~rinv2 correct?

## Slide 52: Plotting Δt over η-1
Is the assumption L2~rinv2 correct?
Plot Δt over η-1 directly to inspect assumption, rinv = const.

## Slide 53: Plotting Δt over η-1
Is the assumption L2~rinv2 correct?
Plot Δt over η-1 directly to inspect assumption, rinv = const.

## Slide 54: Plotting Δt over η-1
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 55: Plotting Δt over η-1
Small data set causes low R2 value
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 56: Plotting Δt over η-1
Overall very good reliability
Small data set causes low R2 value
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 57: Plotting Δt over η-1
Overall very good reliability
Average exponent of b = -1.63±0.14
Small data set causes low R2 value
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 58: Plotting Δt over η-1
Overall very good reliability
Average exponent of b = -1.63±0.14
Disadvantages of scaling method:
  several hidden dependencies in η
  Dependencies influence each other
Small data set causes low R2 value
Difficult to examine
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 59: Plotting Δt over η-1
Overall very good reliability
Average exponent of b = -1.63±0.14
Disadvantages of scaling method:
  several hidden dependencies in η
  Dependencies influence each other
→ assumption L2~rinv2 may be incorrect
Small data set causes low R2 value
Difficult to examine
Fit parameters (y = a + x∙b) and R2 for all discharges:

## Slide 60: Summary
Most reliable scaling method: Δt over rinv/a

## Slide 61: Summary
Most reliable scaling method: Δt over rinv/a
  Results deviate from hypothesis
  → hypothesis could not be confirmed

## Slide 62: Summary
Most reliable scaling method: Δt over rinv/a
  Results deviate from hypothesis
  → hypothesis could not be confirmed
Scaling method Δt over η-1 very reliable

## Slide 63: Summary
Most reliable scaling method: Δt over rinv/a
  Results deviate from hypothesis
  → hypothesis could not be confirmed
Scaling method Δt over η-1 very reliable
  Possibly the assumption L2~rinv2 is incorrect
  → what is L?

## Slide 64: Summary
Most reliable scaling method: Δt over rinv/a
  Results deviate from hypothesis
  → hypothesis could not be confirmed
Scaling method Δt over η-1 very reliable
  Possibly the assumption L2~rinv2 is incorrect
  → what is L?
  Dependencies in η unknown

## Slide 65: Summary
Most reliable scaling method: Δt over rinv/a
  Results deviate from hypothesis
  → hypothesis could not be confirmed
Scaling method Δt over η-1 very reliable
  Possibly the assumption L2~rinv2 is incorrect
  → what is L?
  Dependencies in η unknown
Which parameters influence τR and how? Could this help verify τR~Δt?

## Slide 66: PCA
Principal Component Analysis (PCA):
  Orthogonal linear transformation reduces dimensionality of data sets

## Slide 67: PCA
Principal Component Analysis (PCA):
  Orthogonal linear transformation reduces dimensionality of data sets
Principal components:
  Describe the data set through linear functions
  Preserve as much variance as possible

## Slide 68: PCA
Principal Component Analysis (PCA):
  Orthogonal linear transformation reduces dimensionality of data sets
Principal components:
  Describe the data set through linear functions
  Preserve as much variance as possible
Parameters used in the PCA:
  Inversion radius rinv
  Electron temperature Te
  Respective radial derivative dT/dr
  Crash amplitude ΔT
  Electron density ne
  Toroidal current Itor
  Heating power PECRH
  Diamagnetic energy Wdia
  Effective resistive time <τR>
  Plasma resistivity ηZavg with an average atomic number

## Slide 69: PCA – PC1 and PC2
10 parameters reduced to 6 through PCA analysis

## Slide 70: PCA – 3D plot
PCA results compared with Δt
  Δt given in the color gradient of the crashes (lighter dots ~ larger Δt)

## Slide 71: Conclusion
Hypothesis of Δt ~ τR couldn’t be confirmed, with
  Obvious trend BUT same scaling not found

## Slide 72: Conclusion
Hypothesis of Δt ~ τR couldn’t be confirmed, with
  Obvious trend BUT same scaling not found
Plotting Δt over η-1 yields very reliable results
  Assumption of L2 ~ rinv2 incorrect?
  → what is L?

## Slide 73: Conclusion
Hypothesis of Δt ~ τR couldn’t be confirmed, with
  Obvious trend BUT same scaling not found
Plotting Δt over η-1 yields very reliable results
  Assumption of L2 ~ rinv2 incorrect?
  → what is L?
Larger data sets needed for further research and more reliable results → future experiments planned

## Slide 74: Conclusion
Hypothesis of Δt ~ τR couldn’t be confirmed, with
  Obvious trend BUT same scaling not found
Plotting Δt over η-1 yields very reliable results
  Assumption of L2 ~ rinv2 incorrect?
  → what is L?
Larger data sets needed for further research and more reliable results → future experiments planned
PCA is a good starting point for further research into sawtooth instabilities
  → Could a multiple-parameter fit verify the hypothesis?

## Slide 75: Comparison of all scaling methods
Δt over rinv/a
Δt over τR,inv
Δt over <τR>
Average R2: 0.79
Average R2: 0.35
Average R2: 0.64
Average exponent: b = 3.12±0.98
  Expected is 2
b deviates from expected value
  η(rinv) increases discrepancy
Average exponent: b = 2.73±0.79
  Expected is 1
Influence of Zeff shown
  Unreliable results
  Other influences possible
b nears expected value BUT percentage error >100%
→ unreliable results
Average exponent: b = 1.07±1.15
  Expected is 1
Highest reliability
Unreliable scaling method
Δt over rinv/a
Δt over τR,inv
Δt over <τR>
Average R2: 0.79
Average R2: 0.35
Average R2: 0.64
Average exponent: b = 3.12±0.98
  Expected is 2
b deviates from expected value
  η(rinv) increases discrepancy
Average exponent: b = 2.73±0.79
  Expected is 1
Influence of Zeff shown
  Unreliable results
  Other influences possible
b nears expected value BUT percentage error >100%
→ unreliable results
Average exponent: b = 1.07±1.15
  Expected is 1
Highest reliability
Unreliable scaling method