## Slide 1: Analysis of the fast-ion distribution in W7-X from the Balmer-alpha spectrum
Peter Zs. Poloskei*, O. Ford, B. Geiger and many important others
*peter.poloskei@ipp.mpg.de

## Slide 2: Motivation
W7-X was designed for good fast-ion confinement in high-β:
  Optimized, „good” neoclassical particle orbits
  Diagnosing this feature is a goal of W7X
Tasks to be done:
  Investigate the current capabilities of the CXRS system to infer properties of fast-ions
  Support observation with predictive modelling with FIDASIM
  Understand fast-ions behavior in current low-β plasmas (what influences their confinement)
  Carry out predictive modelling for future high-β plasmas
  Fine-tuning the current system for (even) „better” measurements

## Slide 3: How do we want to diagnose confined fast-ions?
We need fast-ions… → NBI
  Provides fast-ions (Einj ~ 50 keV)
  Provides neutrals what…
…makes active charge-exchange possible
By investigating hydrogen Balmer-alpha emission (Hα)
  n = 3→2 transition, λ0 = 656.281 nm
  max(Δλ) ≈ 6 nm (from fast-neutrals)
  Broad spectral feature expected
CXRS system happens to have a „red“ spectrometer measuring 647-667 nm range
AUG – cold Hα
NBI geometry

## Slide 4: CXRS system in W7-X for detecting Hα
3 different observation directions:
  53 line of sights (LOS) total
  Covering most of the confined region along the NBI
  Different characteristic Doppler-shifts
Absolute intensity calibrated measurement → [Ph/sr/nm/m2/s]
Detailed modelling required for the understanding of the spectrum
  FIDASIM → predicts the Hα spectrum
Beam emission
Impurity lines
Cold Hα
Thermal Hα (Halo)
Radiance Ph/sr/nm/m2/s
Bremsstrahlung
Fast-ion Hα (FIDA)

## Slide 5: FIDASIM – Monte Carloing neutrals
FIDASIM models spatial evolution of different neutral populations, state resolved, solving a collisional-radiative model (excitation, ionization, CX):
  Magnetic equilibrium
  Assumed plasma profiles
  Beam- and observation parameters required
Predicts emissivity of characteristic neutral populations:
  Beam neutrals → from NBI
  Halo neutrals →
  Fast-neutrals →
Predicted spectral shape matches well
20180823.037@5.6s
@ASCOT fi distribution
Efull
Ehalf
Ethird

## Slide 6: How „good“ is FIDASIM‘s Hα estimate?
Checking absolute intensities
  By scaling predicted spectral intensity to match CXRS measurement
BES predicted matches
  Both with measurement
  And calorimetry power prediction
Halo emission discrepancies
  Currently assuming Zeff = 1.5 flat
  Cold neutral – thermal CX?
FIDA emission discrepancies
  Significant O(102) more measured intensity in the edge than predicted
  Too low ASCOT predicted fast-ion density?
  Too low amount of neutrals (for CX)?

## Slide 7: Weight-function estimates of different ports
Current LOS setup is not optimized for FIDA measurements
  Typically high BES Doppler-shift
  No observable temporal evolution τsd < 1/fsampl
Which part of the fast-ion distribution can contribute to given wavelength bin
Port | BES (Doppler-shift) | Co-passing ptc emission | Cntr-passing ptc emission
A | Red (+) | Red | Blue
M | Blue (-) | Blue | Red
T | Red (+) | Blue | Red
Co-passing particles
Counter-passing particles
Weight functions – AET21:14
650.9 nm
651.9 nm
652.9 nm

## Slide 8: Discrepancies in the FIDA spectra
What we observe:
  Too low amount of predicted emission (discrepancy increases towards the edges)
  „Missing“ hump in the co-passing 2nd energy component (fall off responds to changing acceleration voltage)
  No passive FIDA emission observed in different segment (cold neutrals + fast-ions)
Significant amount of edge neutrals?
Hypothesis:
  NBI causes intensive, local recycling
  Causing significant, local passive FIDA emission
  Causing further fast-ion losses through CX
[courtesy A. J. van Vuuren]
Passive CXRS

## Slide 9: Summary
FIDASIM was successfully adapted to W7X geometry, providing:
  Predictive modelling for the Balmer-alpha spectra
  Support for other CX based measurements
Different spectral shapes (BES, halo, FIDA) are well-reproducible with FIDASIM
  Minor discrepancies in absolute intensities, causes under investigation
  Major discrepancies in the edge FIDA observations → missing cold, local neutrals? Possible to be included in the modelling
Sensitivity of the current CXRS LOS setup was investigated
  Current alignment only allows limited investigation of the fast-ion distribution
    T and M port are useful in current setup
  Optimization of the system would be possible for FIDA measurements
    focusing on co-passing particles
    Optimizing BES Doppler-shift with better channel allocation

## Slide 11: Island power losses
In „high-mirror” NBI fires across island
  Electron density can be still high (ne ~ O(1013) cm-3)
  Δl = 4-5 cm
Investigating beam attenuation in a marginal case
  Assuming flat profile based on Thomson’s last measured point in the confined region
20180823.037 @5.2s
  E0 = 48 keV, ne = 4.6 1013 cm-3, Te = 100 eV
SOL NBI power losses 2-12%
Low SOL density is desirable for proper core heating
R [m]
z [m]
Δl

## Slide 12: Neutral densities