## Slide 1: Tools required for divertor design
EMC-lite
  Speed up using trajectory recording schemes
  Understanding of lost particles (visualising path)
  Robust inclusion of arbitrary closed targets
  Validation of shadowing / transport mechanisms with relevant experiments
Smolid including scaling laws from experiments
Magnetic topology toolbox (Target plate independent)
  Automised determination of X- and O-points, separatrix, divertor stagnation front, local island iota
Including targets
  Understanding heat loads from magnetic topology (quantify effect of perpendicular diffusion)
  Automised target shape design tools from magnetic topology
    2-step approach: catch load on perpendicular plate  spread load by plate inclination
    Tracing approach: Defining shape in single toroidal section  deviate from traced contour in subsequent sections. Use shaded area for target shapes of other configurations.
    Develop pre- and postprocessing tools to quickly evaluate designs
  First-flight neutral model (cosine law starting from target surface)
    Ion density in the steady state SOL  re-ionisation path of neutrals  neutral density  updated ion density ?
  Collaboration with Nassim for simple particle exhaust modelling