## Slide 1: Multi-Species Impurity Transport Studies in Stellarators: Status and Prospects A. Langenberg1, M.J. García-Regana2, A. Dinklage1, M. Kubkowska3, Th. Wegner1, B. Buttenschön1, N. Pablant4, F. Reimold1 1 Max-Planck Institute for Plasma Physics, Greifswald, Germany 2 Laboratorio Nacional de Fusión Ciemat, Madrid, Spain 3 Institute of Plasma Physics and Laser Microfusion, Warsaw, Poland 4 Princeton Plasma Physics Laboratory, Princeton, USA

## Slide 2: Motivation / Status
Theoretic predictions for impurity transport
Neoclassical theory:
        Significant variation of transport times t I for Si12+ W44+ impurities
        Absolute values of t I in the order of several seconds
Turbulent transport simulations:
        No Z or M dependence for impurity transport predicted [1]
  Experimental Observations in W7-X [2,3] and LHD [4]
        No / weak Z or M dependence
        Absolute t I ~ 100 – 500 ms
        Turbulence reduced scenarios of W7-X:
          Significantly higher t I in the order of seconds (initial results available, to be verified)
          Z dependence in turbulence reduced scenarios unexplored
[1] P. Helander and A. Zocco Plasma Phys. Control. Fusion (2018)
[2] A. Langenberg, Th. Wegner, N. Pablant et al. Phys. Plasmas (2020)
[3] M. Kubkowska, A. Czarnecka, T. Fornal et al. Rev. Scien. Instrum. (2018)
[4] N. Tamura, M. Yoshinuma, K. Ida et al. Plasma and Fusion Research (2021)

## Slide 3: Motivation / Status
Recent theoretical findings with the GK code stella [4]
        Except for LHD, ITG-driven transport of impurities in W7-X is not particularly higher w.r.t. other machines.
        Increasing main ion density gradient  turbulent transport coefficients in W7-X drop up to factor of ~8.
        Including non-trace impurities can strongly impact turbulent heat fluxes in W7-X
          Non-trace impurities with same sign of density gradient as main ions  turbulence suppresion.
          Non-trace impurities with opposite sign of density gradient as main ions  turbulence enhancement.
        [García-Regaña EPS´22]
[4] J.M. García-Regana, M. Barnes, I. Calvo et al. Nuclear Fusion (2021)

## Slide 4: Ideas for Cross Machine Experiments
Z dependence cross comparison:
        measure t I for Si12+ W44+ impurities in W7-X, LHD, …? medium density plasmas
        status W7-X:
          turbulence dominated ECRH plasmas t I data available
          no data for high performance NBI plasmas (experiments for OP2.1 planned)
        status LHD:
          signs of weak Z dependence in med ne LHD plasmas
          to be repeated with wider variation of impurities incl. W?
  Matching experiments in NBI plasmas:
        match Te, ne profiles of W7-X and LHD in medium density NBI plasmas for a direct t I comparison
        varying Z if possible
  Questions:
        observable impurity species in LHD, W?
        matching Te, ne profiles in W7-X and LHD NBI plasmas traight forward?
        other machines to be included (TJ-II)?

## Slide 5: Impurity Diagnostics / Transport Parameter Access
LHD | W7-X | TJ-II | H-J | HSX | AUG/TE | other
t I (Z) | t I (Z) |  |  |  |  | 
∫ nZ dl, nZ (r) B,C, Si, W | ∫ nZ dl, nZ (r) C, Ar, Fe |  |  |  |  | 
D+v (r) C | D+v (r) C, Ar, Fe |  |  |  |  | 
 | G (r) Ar, Fe |  |  |  |  | 
2xTESPEL, IPD | LBO, TESPEL, IPD |  |  |  |  | 
E/VUV-Spec, CXS, Tomography? | XICS, PHA, CXRS, VUV-Spec, Tomography |  |  |  |  |