## Slide 1: TG: Core Performance and Scenario Development - Profile Control - A. Langenberg and J. Proll on behalf of the W7-X Team Max-Planck Institute for Plasma Physics, Greifswald, Germany

## Slide 2: Outline
Main Topics
        Advanced Scenarios
        Transport and Impurtiy Control: Topical Overview
        Profile Control (A. Langenberg)
Paper Rehearsal
        CXRS He/H Concentration Measurements (Katsumi Ida-san)
        Validation of a Comprehensive First- Principles-Based Framework for Predicting the Performance of Future Stellarators (Agapito Fernando)

## Slide 3: III. Profile Control
  Profile measurements / data analysis / data availability (ROs of diagnostics)
    list of profiles routinely required: Te , Ti , ne , Zeff , nZ , Er , PECRHabsorbed , PNBIabsorbed … ?
        state of the art (ToDos?) for data analysis and evaluation ?
        commissioning requirments for profile diangostics (e.g. high Te scenario, reference program…) ?
    profile cross validations after diagnostic updates / longer W7-X shutdowns
    balance profile requirements vs. availability (ROs vs. users)
  Profile shaping
    ne profile shaping
        deterministic recipes for ne shaping (e.g. low ECRH, NBI+ECRH, pellets) -> theoretic modeling ?
        heat and particle transport (data and modeling)
        pellet deposition, event based triggering of pellets
    Ti/e and Er profile shaping (CERC to IRC transitions), deterministic recipes (NBI, ECCD, …), scaling ?
    real time profile control -> real time profile data

## Slide 4: III. Profile Control: Data Availability
Diagnostic | Parameters | Intershot Data | Overview Plot + Archive | Profiles for publication | Archive Links | ToDos
Thomson scattering | Te and ne profiles Dt = 30 ms | uncalibrated profiles | √ √ | on request |  | automatic profiles ready for publication
Interferometer | ne line int. Dt = 100 µs | Line int. ne | √ √ | - |  | fix calibration issue
ECE | Te profiles Dt = 1 µs | rad. temp. | √ √ | on request |  | automatic profiles ready for publication
XICS | Te + Ti profiles Er profiles Dt = 100 ms | central Te + Ti | √ √ | over night Er on request |  | automatic Er analysis
CXRS | Ti+nZ+Er profiles nH/nHe ratio Dt = 10 ms | central Ti nH/nHe | √ √ | Er on request |  | automatic Er analysis
Diam. loops | Wdia Dt = 10 µs | Wdia | √ √ | - |  | Accomplished.
Tomography | 2D impurity patterns | nZ time traces | - - | on request |  | automatic tomography
Bolometer | 2D radiation patterns | frad time traces | √ √ | on request |  | automatic tomography
Zeff | Zeff | - | - - | - |  | RO: M. Krychoviak and S. Serada
PECRH absorbed | absorbed PECRH | - | - - | - |  | RO: T. Stange
PNBI absorbed | absorbed PNBI | - | - - | - |  | RO: N. Rusk + N.N.

## Slide 5: III. Profile Control: OP2.3 Reference Programme
    unchanged to OP2.2
    if energy extension allows: extension to 28 s for wall conditioning
Courtesy of D. Naujoks

## Slide 6: Links and Mails
  Indico Website of TG: https://event.ipp-hgw.mpg.de/category/123/
    Schedules for planned TG-meetings
    Archiving of TG-meetings incl. talks via slides and minuites
    Link to join TG-meeting online:
    https://ipp-meet.webex.com/ippmeet/j.php?MTID=m98b5c7ba393c66f0fd8e3d389e11d755
  Mailing list of TG:
    Announcement and reminders for TG-meetings and their agenda
    Join: w7x-tg-core-performance-scenarios-join@ipp.mpg.de

## Slide 7: …

## Slide 8: Backups