## Slide 1: Investigation of methane pyrolysis and dry reforming of methane in microwave plasma
Clemens Kranig
Scientific Supervisor: Dr. Ante Hecimovic
Academic Supervisor: Prof. Dr. Ursel Fantz

## Slide 2: A little bit about myself

## Slide 3: Research history I
B.Sc. Mechanical Engineering @ TUM -> Modeling of pyrolysis in a wire mesh reactor
M.Sc. Energy and Process Engineering @ TUM
Semester Thesis: Conceptual Design of Pyrolysis reactor using a plasma cutter as source
T [°C] | p [bar] | t [s] | H [K/s]
400-1600 | 1 – 40 | 1 – 10 | 10 - 1000
Pyrolysis is an important step within the gasification process
Pyrolysis reaction kinetics used as an input for a larger CFD - simulation
Investigation of direct contact of different fuel particles (biomass, coal, plastic) with the plasma
Replacing larger fossil fuel powered burners in gasification reactors with plasma torches

## Slide 4: Research history II
Master Thesis at TUM and IPP:
Design of the in-vessel stabilization coils in saddle configuration for DEMO
Left: continuous toroidal configuration
Right: saddle configuration
Saddle configuration of in-vessel coils makes them easier to access

## Slide 5: PhD at IPP - Plasma for gas conversion (P4G)
Conversion of different molecules within the framework of Power-to-X and electrification of chemical processes
Plasma
Stabilization of different plasma conditions
Determination of dominant conversion mechanisms
Improvement of plasma processes towards higher conversion and higher energy efficiency based on the dominant conversion mechanism
CH4 + CO2
CH4
CO2
NH3
N2 + H2
CO + H2
Cs + H2
CO + O2
N2 + H2
NH3
Synthesis gas for Fischer-Tropsch processes or MeOH synthesis
Hydrogen production
Alternative to energy intense Haber – Bosch process
Ammonia as energy carrier or for fertilizer production
Electrical energy from renewable energy sources

## Slide 6: Dry reforming of methane (DRM) and CH4-pyrolysis
CH4-Pyrolysis:
DRM:
Thermodynamic Equilibrium
Endothermic reactions → much energy required to enable forward reaction
On an industrial scale processes involving these reactions are realized by thermo-catalytic methods, high temperatures provided by burning of fossil fuels
Plasma creates alternative paths for the conversion process apart from thermodynamic equilibrium

## Slide 7: Experimental setup of a microwave plasma torch
7
Coaxial resonator
Three-stub-tuner
Gas chromatograph
Mass spectrometer
Power supply
2.45 GHz microwave
Echelle spectrometer
After experiment cold gas analysis
CO2 Plasma
DRM Plasma [CH4]/[CO2]= 1
≈3cm
Temperature in the center of the plasma
up to ≈ 6000K
up to ≈ 4000K
Circulator

## Slide 8: First results on DRM experiments I
Γtot =20slm
Pin = 1.8kW
[H2]/[CO] ratio effectively changed, high remaining [CH4] & [CO2] after the plasma
For equilibrium condition with T ≥ 1000K: no CO2 or CH4 in equilibrium compositions
Equilibrium composition not directly applicable, however together with temperature measurements of the plasma leads to better understanding of the conversion process

## Slide 9: Next steps and outlook
Further experiments with Biogas compositions ([CH4]/[CO2] ≈ 60/40), biogas impurity test
Extended parameter studies for higher CH4 concentrations ([CH4] > 60%) in the feed
Improvement of diagnostic/measurement procedure for more accurate determination of gas compositions
Understanding the conversion process of CH4 with microwave plasma to compare microwave plasma for CH4 conversion
to other plasma sources
to other thermal processes
Thank you very much for your attention!

## Slide 10: First results on DRM experiments II
Experimental results for different specific energy inputs at 1bar
[CO2]/[CH4] = 7/3
Γtot = 6-40slm
Pin = 1.2 – 2.64 kW
Increased CO2 and CH4 conversion without significantly changing the H2/CO ratio