## Slide 1: Overview of the impurity injection studies and remaining work for LHD Federico Nespoli
PPPL: R. Lunsford, A. Nagy, N.A. Pablant
LHD (Japan): N. Tamura, M. Nunami, K. Tanaka, S. Masuzaki, M. Shoji
W7-X (Germany): T. Wegner, C. Killer, D. Cipciar, B. Buttenschon
CIEMAT (Spain): I. Garcia Cortes, A. De Castro Calles, D. Medina Roque, K. Maccarthy
CWGM, PPPL, June 4th 2025

## Slide 2: Outline
  Background: low Z powder injection improved stellarator performance
  LHD:
  Turbulence reduction and improved confinement
  W7-X:
  Confinement improvement with pulsed powder injection
  JE to directly compare effect of impurity powder across machines
  LHD results
  W7X results
  TJ-II results
  Comparison with B LBO
  Next steps

## Slide 3: Developing real time boronization in steady state operation
Maintaining good wall conditions is a challenge for metal walls, steady-state reactors
Real time boronization by injecting boron powder into the plasma with the Impurity Powder Dropper:
  no toxic gas
  no interruption of operation
  more mass-efficient
Already been tested in tokamaks (DIIID, ASDEX-U, EAST, WEST, KSTAR)
Improved plasma performances accessing lower collisionalities through lower wall recycling and impurity content
LHD capable of 1 hour long discharges: assess the viability of real time boronization in steady state operation with IPD
outboard
toroidal

## Slide 4: Access to a reduced turbulence improved confinement regime
Increase of Te and Ti sometimes observed during B powder injection
Matched discharges with same density and power
Ti can increase up to ~ 50%
At the same time, turbulent density fluctuations decreased up to a factor 2 across plasma volume
Observed with
  various heating schemes
  both D and H plasmas
  both directions of magnetic field
  [Nespoli Nat Phys 2022]
Extensive experiments scanning plasma parameters, powder materials [Nespoli NF 2023]
Reference
B powder
No data
Ti ~ +25%
Te ~ +25%

## Slide 5: Suppression of ion scale turbulence possible cause of improvement
ITG-like lower frequency turbulence damped, TEM-like higher frequency excited.
Presence of both ITG and TEM confirmed by gyrokinetic simulations [Singh NF 2023]
ITG reduction can be due to
  Profile modification
  Increase in Zeff
Reference
B powder
Reference
B powder

## Slide 6: Powder injection in W7-X with the PMPI
Probe Mounted Powder Injector: A reduced version of IPD that fits on a reciprocating probe [Nagy FED 2019]
B4C powder injected horizontally in pulses by a paddle wheel
First set of experiments showed an increase of Ti above the Ti-clamping level and reduction of turbulence [Lunsford PoP 2021]
Effect on Te and Wp remain transitory
Possibly same mechanism at play as in LHD, could be steady-state with continuous powder flow

## Slide 7: Joint experiment on effect of impurity on stellarator performance
Objectives:
Directly compare effect of boron powder impurities on stellarator performance across different machines
  temperature increase
  turbulence reduction
  Inject powder in “identical” plasmas [Warmer PRL 2021]
Compare different injection techniques
  Continuous –pulsed (LHD)
  Powder – B LBO (W7-X)
LHD
W7-X
TJ-II/HSX
Te
ne
powder
LBO

## Slide 8: LHD experiments
B powder injected in plasmas
3 scenarios:
  TJ-II ne=0.5e19 PECH =0.7MW
  W7-X Warmer PRL ne=1.5e19 PECH=2MW
  W7-X Lunsford PoP ne=5.2e19 PECH =4MW
1) Ti increases but Te decreases. ne increases (no density control)
2) Te and Ti increase
3) Te increases, Ti not clear more analysis needed
Additional heating phases require more analysis (pNB only to mimic W7-X)
POWDER

## Slide 9: LHD experiments
B powder injected in plasmas
3 scenarios:
  TJ-II ne=0.5e19 PECH =0.7MW
  W7-X Warmer PRL ne=1.5e19 PECH=2MW
  W7-X Lunsford PoP ne=5.2e19 PECH =4MW
Effect on turbulence:
1) turbulence increased
2) turbulence spectrum changed
3) turbulence reduced
Somewhat in line with previous experiments in LHD
Low density (TJ-II -like)
Mid density (W7-X Warmer -like)
High density (W7-X Lunsford -like)
reference
B powder

## Slide 10: LHD experiments
Comparison continuous- pulsed
Attempted pulsed powder injection 0.2s on/off to mimic PMPI on W7X
Each pulse spreads in time during powder free fall, superimposing
Gives almost continuous flow but with lower mass rate

## Slide 11: W7-X experiments
New set of experiments in March 2025
3 scenarios:
  Warmer PRL ne=1.5e19 PECH=2MW
  ne=3e19 PECH =2MW +PNBI=1.6 MW
  ne=3e19 PECH =4MW
[Courtesy of C.Killer]

## Slide 12: W7-X experiments
New set of experiments in March 2025
3 scenarios:
  Warmer PRL ne=1.5e19 PECH=2MW
  ne=3e19 PECH =2MW +PNBI=1.6 MW
  ne=3e19 PECH =4MW
Clearer improvement of performances(Ti, Wp) during ECH +NBI heating
Turbulence reduced in between pulses (PCI)

## Slide 13: W7-X experiments
New set of experiments in March 2025
3 scenarios:
  Warmer PRL ne=1.5e19 PECH=2MW
  ne=3e19 PECH =2MW +PNBI=1.6 MW
  ne=3e19 PECH =4MW
Clearer improvement of performances(Ti, Wp) during ECH +NBI heating
Turbulence reduced in between pulses (PCI)
[Courtesy of A. von Stechow]

## Slide 14: W7-X experiments
Comparison PMPI/ B LBO
B LBO injected in same plasma conditions, first at ~3Hz
Increasing intensity of the laser
Increase to max frequency 20 Hz
Even in that case, no clear effect on the plasma
Possibly quantity of injected B still too little O(e17)/pulse
More analysis needed

## Slide 15: TJ-II experiments
B4C powder injection attempted using TESPEL mechanism without encapsulation
Only one shot successful, then powder got stuck in revolving mechanism
Compared with B LBO
In both cases no clear effect on Ti, Te drop, ne increase
ref
B LBO
B4C pow

## Slide 16: Next steps
LHD: in last campaign, repeat scenarios used in latest W7-X experiments
W7-X: nothing to be done until OP2.4. A full IPD will be operative by then, more in dept comparison will be possible
TJ-II, HSX: possibility to install a small powder dropper under consideration. Perform more B LBO experiments

## Slide 17: Backup slides
B
BN
Li

## Slide 18: Boron deposited on first wall and divertor
Material sample located at first wall exposed to IPD experiments
deposition of B thin film confirmed by the post mortem optical emission spectroscopy analysis [Lunsford NF 2022]
Emission from BH molecules and B+ ions measured with spatially resolved spectroscopy
BH and B+ are concentrated in the divertor region during powder injection
B ions are deposited on the divertor as well [Kawate NF 2022]
B
H
Fe
C
O (10X)

## Slide 19: Improvement scales with amount of injected powder
Relative improvement of ion and electron temperature increases with amount of injected powder
Increase in confinement time in general positive
Above a mass injection threshold, density control is lost and/or plasma collapses
Turbulence response more complicated, varies with different scenarios
[Nespoli NF 2023]

## Slide 20: Improvement observed with different powder materials
Access to reduced turbulence observed with B, C, BN powders
Similar response for the three materials:
~30% increase of Ti and Te
turbulence decrease inside LCFS and for lower frequencies, increase for higher frequencies and close to LFCS
Reduction of χi and χe for 0.4< reff/a99<0.9 (DYTRANS)
Reduction of intrinsic impurities
Reduction of recycling (even for C)

## Slide 21: Simulations help understanding powder injection
Coupled simulations of EMC3-EIRENE (plasma background) with DUSTT (powder grains dynamics)
Dedicated experiments for model validation
Increasing plasma density, powder ablation point observed to move outwards
Result recovered in simulations, due to increased ion drag in the divertor leg [Shoji, NME 2025]
increasing ne
Outboard side
1.5×1019 m-3
3×1019 m-3
5×1019 m-3
B 150 μm