## Slide 1: Overview of divertors in LHD, AUG, DIII-D and JET regarding ionization, neutralization and pumping
Diploma Thesis

## Slide 2: Introduction
Diploma thesis: Magnetic configuration comparison of hydrogen fueling, recycling and confinement at Wendelstein 7-X via a single-reservoir particle balance
    OP 1.2b: High Mirror, High Iota (attachted Plasmas)
  Supervisor: Thierry Kremeyer
  Date: 01.06. ~ 18.10.2023
  University: TU Dresden
  Mechanical Engineering (Energy Technology)

## Slide 3: Divertor Particle Exhaust Efficiencies
Bad particles Good particles
Particle exhaust efficiencies
ηexhaust = ΓExhaust / ΓNeutral = ηcollection * ηremoval
Particle collection
ηcollection = ΓPumpgap / ΓNeutral
Particle removal
ηremoval = ΓExhaust / Γpumpgap
Particle plugging
ηplugging = ΓDivertor Recycling / ΓRecycling
Core Edge Divertor Pumpgap Sub-divertor
(Plasma + Neutrals) (Neutrals)
Γexhaust
Reff * ΓNeutral
ΓNeutral
Γpumpgap
Γion divertor
Γdiv-recy
Γsub-div loss
Γedge-recy
[T. Kremeyer]
[T. Kremeyer]
Notes: Particle exhaust after neutralisation – hard boundary condition is to keep rho below 10, and for a steady state reaction we need to exhaust as much He as is formed in the fusion reaction.
Divertor exhaust metric, how many of the neutralized particles are exhausted
  Seperate into collection, what fraction of particles from the strike line make it into the sub-divertor
  Removal, what fraction of the particles in the sub-divertor is removed
  Additionally plugging: Keep particles that aren‘t exhausted in the divertor. Another chance for exhaust, minimize CX
Neutralize on targets – plasma wall interaction - Impurities out of confined plasma
  Minimize erosion, Te
  Can‘t fully avoid it, keep erosion away from LCFS, so that impurities can ionize in SOL
*Click* These targets have to be engineered
  Handle the heat loads
  Materials that survive nuclear conditions
*Click* This talk has the goal to extrapolate design metrics for particle exhaust, based on the fuel cycle at W7-X

## Slide 4: Divertors in LHD

## Slide 5: Helical Divertor (HD)
first divertor(3)
left inner-port, right outer-port
total pumping speed S ~ 140 – 400 m3/s(1,2)
effective pumping speed Seff ~ 9 m3/s(5)
neutral pressure pn ~ 10-2 Pa (entrance of pump system)(2)
neutral flux at divertor Γdiv ~ 1020 – 1023 m-2 s-1(4)
ionized and exhausted particles ~ 25% of input particles(2)
(3)
(4)

## Slide 6: Local Island Divertor (LID)
first operation 2002(7)
left inner-port, right outer-port
in combination with HD(7)
pumping speed S ~ 200 m3/s(2)
neutral pressure pn ~ 10-1 Pa(2)
ionized and exhausted particles ~ 70%(2)
90% recycling LID, 10% main chamber(7)
pumping efficiency without recycling 50 – 60% (modeling)(7)
(6)

## Slide 7: Closed Helical Divertor (CHD)
first operation 2010(9)
left inner-port, right outer-port(8)
effective divertor pumping speed Seff ~ 70 m3/s (inner-port)(10)
main pumping speed S ~ 220 m3/s (outer-port)(10)
neutral pressure behind dome pn ~ 10-1 Pa(11)
gas puff exhausted by:(10)
    divertor pump ~ 50%
    main pump ~ 5%
    wall ~ 45%
Ratio of molecular hydrogen density at cryo pump to divertor plate ~ 16% (modeling)(12)
(8)
(8)

## Slide 8: Divertors in ASDEX Upgrade

## Slide 9: Div I
first divertor(13)
effective pumping speed in divertor Seff ~ 13 m3/s(14)
neutral flux at divertor Γdiv ~ 1022 – 1023 m-2 s-1(13,14)
ion flux in divertor:(15)
    ΓInner target ~ 2 x 1022 s-1
    ΓInner recombination ~ 6 x 1022 s-1
    ΓOuter target ~ 6 x 1022 s-1
volume recombination rate coefficient ~ 10-18 m3/s(15)
volumen recombination is 3x bigger than neutralization at inner target, but weak in outer divertor(3)
(13)
(14)

## Slide 10: Div II
first operation 1997(20)
effective pumping speed Seff ~ 100 + 10 m3/s (cryo pump and turbo-molecular pump)(16)
leakage pumping region ~ 100 m3/s(16)
neutral flux at divertor Γdiv ~ 1023 m-2 s-1(13)
neutral flux in subdivertor Γsubdiv ~ 3.5 x 1022 m-2 s-1(16) (35 % Γdiv)
neutral flux in pumping region Γpump ~ 4.5 x 1021 m-2 s-1(16) (12.9 % Γsubdiv )
influx rate Γinflux ~ 0.5 – 20 x 1021 s-1 is ~ 20 times smaller than fluxes from recycling in subdivertor(18)
neutral removal rate ~ 275 A(16)
At high Te plasma in front of targets is opaque to neutrals from private flux region(18)
volume recombination rate coefficient ~ 10-16 m3/s(17)
ratio neutral flux in pumping chamber to sub-divertor ~ 0.22 (modeling)(19)
(13)

## Slide 11: Div II

## Slide 12: Div III
first operation 2013(19)
neutral pressure pn ~ 4 Pa(19)
pumping efficiency increased by ~ 30% (modeling)(19)
ratio neutral flux in pumping chamber to sub-divertor ~ 0.28 (modeling)(19)
(19)
(19)

## Slide 13: Divertor in DIII-D

## Slide 14: Divertor
effective pumping speed Seff: (23,25)
    ~ 40 m3/s at ~ 0.66 Pa for D2
    12 – 14 m3/s for He
ion flux at target Γtarget:(22)
    1.25 x 1022 s-1 (±0.85 x 1022 s-1)
    1 – 5 x 1022 s-1 (modeling)
cryo exhaust Γcryo ~ 1020 – 1021 s-1(24)
plasma efflux Γefflux ~ 1022 s-1(24)
pumping efficiency 4 – 8 % (open and closed configuration)(24)
wall pumping efficiency 7 – 9 %(24)
volume recombination mostly above target surface(26)
(21)

## Slide 15: Small Angle Slot Divertor (SAS)
(21)
(27)
goal:(28)
radiation to distribute heat flux
baffle with slot to minimize Reff

## Slide 16: Divertors in JET

## Slide 17: Mark I
first operation 1994(17)
pumping speed S ~ 200 + 10 m3/s (cryo and turbomolecular pump for D2)(32)
~ 80% for He(32)
neutral pressure pn:(29)
    0.37 x 10-20 m3Pa x e – 0.61 x 10-1 Pa
(13)

## Slide 18: Mark IIA(P)
first operation 1996(29)
pumping speed S ~ 200 m3/s(30)
neutral pressure pn:(29)
    1.1 x 10-20 m3Pa x e – 1.68 x 10-1 Pa
ion flux at target Γtarget:(33)
    3.08 x 103 m3s-1 x e – 1.77 x 1022 s-1
hydrogen ionization above X-point 5 – 20%(33)
(13)

## Slide 19: Mark IIA(P)
first operation 1996(29)
pumping speed S ~ 200 m3/s(30)
neutral pressure pn:(29)
    1.1 x 10-20 m3Pa x e – 1.68 x 10-1 Pa
ion flux at target Γtarget:(33)
    3.08 x 103 m3s-1 x e – 1.77 x 1022 s-1
hydrogen ionization above X-point 5 – 20%(33)

## Slide 20: Mark IIGB
first operation 1998(29)
pumping speed S ~ 200 m3/s(30)
neutral pressure pn:(29)
    2.28 x 10-20 m3Pa x e – 4.03 x 10-1 Pa
ion flux at target Γtarget 6 – 30 x 1022 s-1 (Rc = 0.95 and 0.99, modeling)(31)
neutral particle flux in subdivertor Γsubdiv ~ 9.8 x 1021 s-1(30)
divertor gaps 0.08 m and 0.082 m(30)
capture coefficient 15%(30)
subdivertor removal rate ≤ 16% (modeling)(30)
(13)

## Slide 21: Mark IIGB
(13)
(29)
Γexhaust for e = 3 x 1019 m-3:
Mark I ~ 4.82 x 1021 s-1(29,32 calc.)
Mark IIAP ~ 1.56 x 1022 s-1(29,30 calc.)
Mark IIGB ~ 2.72 x 1022 s-1(29,30, calc.)

## Slide 22: Particle Exhaust Efficiencies general Overview
Experiment | LHD |  |  | AUG |  |  | DIII-D | JET |  | 
Divertor | Helical Divertor | Local Island Divertor | Closed Helical Divertor | Div I | Div II | Div III |  | Mark I | Mark IIAP | Mark IIGB
ΓNeutral | 1020 – 1023 m-2s-1(5) | 1.6 – 1.9 x 1022 s-1 (2,7 calc.) | 6.8 x 1021 – 2.1 x 1022 s-1 (10,11,12 calc.) | 1.4 x 1023 s-1(15) | 1023 m-2s-1(13) |  | 1022 s-1(22,24) |  | 5.9 x 1022 s-1 (33 calc.) | 6 – 30 x 1022 s-1(31 mod.)
ΓPumpgap | ~ ΓExhaust | ~ ΓExhaust |  |  | 3.5 x 1022 m-2s-1(16) |  | ~ ΓExhaust |  |  | 9.8 x 1021 s-1
ΓExhaust | 4.35 x 1019 s-1(2,5 calc.) | 9.66 x 1021 s-1(2 calc.) | 3.38 x 1021 s-1(10,11 calc.) |  | 4.5 x 1021 m-2s-1(16) 1.7 x 1021 s-1(16 calc.) |  | 1020 – 1021 s-1(24) | 4.8 x 1021 s-1 (29,32 calc.) | 1.6 x 1022 s-1 (29,30 calc.) | 2.7 x 1022 s-1 (1.5 x 1021 s-1) (29,30,31 calc.)
ηcollection | — | — |  |  | 35%(13,16 calc.) |  | — |  |  | 3.3% – 16.3%(30,31 calc.)
ηremoval | — | — |  |  | 22%(19 mod.) / 13%(16 calc.) | 28%(19 mod.) | — |  |  | 15%(30) / 16%(30 mod.)
ηexhaust | 0.9%(2,5 calc.) | 50 – 60% (7 mod.) | 16%(12 mod.) |  | 1.7% (13,16 calc.) |  | 4 – 8%(24) |  | (27.1%) (29,30,33 calc.) | 0.5% – 2.4% (0.9 – 45%) (30,31 calc.)
ΓRecycling |  |  |  |  |  |  |  |  |  | 
ΓDivertor Recycling |  |  |  |  |  |  |  |  |  | 
ηplugging |  | 90%(7) |  |  |  |  |  |  |  | 
calc. = own calculation based on values from given papers (for fluxes a temprature of 300K and for JET an S of 200m3/s was assumed); mod. = values from modeling

## Slide 23: Sources

## Slide 24: LHD
S. Masuzaki, M. Kobayashi, M. Tokitani, N. Ashikawa, T. Hino, Y. Yamauchi, Y. Nobuta, N. Yoshida, M. Miyamoto, R. Sakamoto, J. Miyazawa, T. Morisaki, N. Ohyabu, H. Yamada, A. Komori & LHD Experiment Group (2010) Fuel Retention in LHD, Fusion Science and Technology, 58:1, 321-330, DOI: 10.13182/FST10-A10818
Masuzaki, S., Kobayashi, M., & Sakamoto, R. (2006). Particle balance study in the Large Helical Device (NIFS--845). Japan
N. Ohyabu et al 1994 Nucl. Fusion 34 387
A Sagara, S Masuzaki, T Morisaki, S Morita, H Funaba, M Goto, Y Nakamura, K Nishimura, N Noda, M Shoji, H Suzuki, A Takayama, A Komori, N Ohyabu, O Motojima, K Morita, K Ohya, J.P Sharpe, LHD Experimental Group, Helical divertor operation and erosion/deposition at target surfaces in LHD, Journal of Nuclear Materials, Volumes 313–316, 2003, Pages 1-10, ISSN 0022-3115, https://doi.org/10.1016/S0022-3115(02)01326-0
G. Motojima et al 2018 Nucl. Fusion 58 014005
Akio Komori, Tomohiro Morisaki, Suguru Masuzaki, Mamoru Shoji, Nobuyoshi Ohyabu, Hiroshi Yamada, Kenji Tanaka, Kazuo Kawahata, Kazumichi Narihara, Shigeru Morita, Byron Jay Peterson, Ryuichi Sakamoto, Satoru Sakakibara, Osamu Motojima, LHD Experimental Group & Hajime Suzuki (2004) Initial Results of Local Island Divertor Experiments in the Large Helical Device, Fusion Science and Technology, 46:1, 167-174, DOI: 10.13182/FST04-A552
T. Morisaki, S. Masuzaki, A. Komori, N. Ohyabu, M. Kobayashi, Y. Feng, F. Sardei, K. Narihara, K. Tanaka, K. Ida, B.J. Peterson, M. Yoshinuma, N. Ashikawa, M. Emoto, H. Funaba, M. Goto, K. Ikeda, S. Inagaki, O. Kaneko, K. Kawahata, S. Kubo, J. Miyazawa, S. Morita, K. Nagaoka, Y. Nagayama, H. Nakanishi, K. Ohkubo, Y. Oka, M. Osakabe, T. Shimozuma, M. Shoji, Y. Takeiri, S. Sakakibara, R. Sakamoto, K. Sato, K. Toi, K. Tsumori, K.Y. Watababe, H. Yamada, I. Yamada, Y. Yoshimura, O. Motojima, Local island divertor experiments on LHD, Journal of Nuclear Materials, Volumes 337–339, 2005, Pages 154-160, ISSN 0022-3115, https://doi.org/10.1016/j.jnucmat.2004.10.165
G Motojima et al 2022 Phys. Scr. 97 035601
Suguru MASUZAKI, Masahiro KOBAYASHI, Mamoru SHOJI, Masayuki TOKITANI, Tomohiro MORISAKI, Ryuichi SAKAMOTO, Masaki OSAKABE, Takanori MURASE, Takashi KOBUCHI, Hiroaki YONEZU, Yasuhiko TAKEIRI, Hiroshi YAMADA, Akio KOMORI, the LHD Experiment Group, Neutral Gas Compression in the Helical Divertor with a Baffle Structure in the LHD Heliotron, Plasma and Fusion Research, 2011, 6 巻, p. 1202007, 公開日 2011/05/20, Online ISSN 1880-6821, https://doi.org/10.1585/pfr.6.1202007
G. Motojima et al 2019 Nucl. Fusion 59 086022
Mamoru SHOJI, Suguru MASUZAKI, Tomohiro MORISAKI, Masahiro KOBAYASHI, Masayuki TOKITANI, Yasuhiko TAKEIRI, Design of a Vacuum Pumping System for the Closed Helical Divertor for Steady State Operation in LHD, Plasma and Fusion Research, 2012, 7 巻, p. 2405145, 公開日 2014/01/10, Online ISSN 1880-6821, https://doi.org/10.1585/pfr.7.2405145
Mamoru SHOJI, Suguru MASUZAKI, Tomohiro MORISAKI, Ryuichi SAKAMOTO, Masayuki TOKITANI, Masahiro KOBAYASHI, Yasuhiko TAKEIRI, Hiroshi YAMADA, Simulation Analysis of the Design of a Vacuum Pumping System for the Closed Helical Divertor in the Large Helical Device, Plasma and Fusion Research, 2011, 6 巻, p. 2401035, 公開日 2012/01/23, Online ISSN 1880-6821, https://doi.org/10.1585/pfr.6.2401035

## Slide 25: ASDEX Upgrade
A Kallenbach et al 1999 Plasma Phys. Control. Fusion 41 B177
H-S Bosch et al 1997 Plasma Phys. Control. Fusion 39 1771
U. Wenzel et al 1999 Nucl. Fusion 39 873
A V Chankin et al 2006 Plasma Phys. Control. Fusion 48 839
U. Wenzel, K. Behringer, K. Büchl, A. Herrmann, K. Schmidtmann, Characterization of the hydrogen emission in divertor II of ASDEX-Upgrade, Journal of Nuclear Materials, Volumes 266–269, 1999, Pages 1252-1256, ISSN 0022-3115, https://doi.org/10.1016/S0022-3115(98)00639-4
A. Scarabosio, G. Haas, H.W. Müller, R. Pugno, M. Wischmeier, Measurements of neutral gas fluxes under different plasma and divertor regimes in ASDEX Upgrade, Journal of Nuclear Materials, Volumes 390–391, 2009, Pages 494-497, ISSN 0022-3115, https://doi.org/10.1016/j.jnucmat.2009.01.057
A. Herrmann et al 2015 Nucl. Fusion 55 063015
Albrecht Herrmann & Otto Gruber (2003) Chapter 1: ASDEX Upgrade - Introduction and Overview, Fusion Science and Technology, 44:3, 569-577, DOI: 10.13182/ FST03-A399

## Slide 26: DIII-D
ITER Physics Expert Group on Divertor et al 1999 Nucl. Fusion 39 2391
M Groth et al 2011 Plasma Phys. Control. Fusion 53 124017
M.A. Mahdavi, S.L. Allen, D.R. Baker, B. Bastasz, N.H. Brooks, D. Buchenauer, R.B. Campbell, J.W. Cuthbertson, T.E. Evans, M.E. Fenstermacher, D.F. Finkenthal, J. Foote, D.N. Hill, D.L. Hillis, F.L. Hinton, J. Hogan, A.W. Howald, A.W. Hyatt, G.L. Jackson, R. Jong, S. Konoshima, C. Lasnier, A.W. Leonard, S.I. Lippmann, R. Maingi, M.M. Menon, P.K. Mioduszewski, R.A. Moyer, H. Ogawa, T.W. Petrie, G.D. Porter, M.E. Rensink, T.D. Rognlein, M.J. Schaffer, K.M. Schaubel, D.L. Sevier, J.P. Smith, G.M. Staebler, G.T. Sager, R.D. Stambaugh, D. Thomas, M.R. Wade, J.G. Watkins, F. Weschenfelder, W.P. West, D.G. Whyte, J. Winter, C.P.C. Wong, R.D. Wood, Divertor heat and particle control experiments on the DIII-D tokamak, Journal of Nuclear Materials, Volumes 220–222, 1995, Pages 13-24, ISSN 0022-3115, https://doi.org/10.1016/0022-3115(94)00443-9
E.A. Unterberg et al 2010 Nucl. Fusion 50 034011
M. R. Wade, D. L. Hillis, J. T. Hogan, R. Maingi, M. M. Menon, M. A. Mahdavi, W. P. West, K. H. Burrell, P. Gohil, R. J. Groebner, R.‐M. Hong, D. H. Kellman, J. C. Phillips, R. P. Seraydarian, the DIII‐D Team, D. F. Finkenthal; Helium transport and exhaust studies in enhanced confinement regimes in DIII‐D. Physics of Plasmas 1 June 1995; 2 (6): 2357–2365. https://doi.org/10.1063/1.871489
M E Fenstermacher et al 1999 Plasma Phys. Control. Fusion 41 A345
H.Y. Guo et al 2019 Nucl. Fusion 59 086054
S.L. Allen, N.H. Brooks, R.B. Campbell, M.E. Fenstermacher, D.N. Hill, A.W. Hyatt, D. Knoll, C.J. Lasnier, E.A. Lazarus, A.W. Leonard, S.I. Lippmann, M.A. Mahdavi, R. Maingi, W. Meyer, R.A. Moyer, T.W. Petrie, G.D. Porter, M.E. Rensink, T.D. Rognlien, M.J. Schaffer, J.P. Smith, G.M. Staebler, R.D. Stambaugh, W.P. West, R.D. Wood, Development of a radiative divertor for DIII-D, Journal of Nuclear Materials, Volumes 220–222, 1995, Pages 336-341, ISSN 0022-3115, https://doi.org/10.1016/0022-3115(94)00495-1

## Slide 27: JET
M Keilhacker and the JET Team 1999 Plasma Phys. Control. Fusion 41 B1
F. Bonelli et al 2017 Nucl. Fusion 57 066037
R Cesario et al 2013 Plasma Phys. Control. Fusion 55 045005
W. Obert, K. Barth, L. Herblin, C. Mayaux, G. Saibene and E. Thompson, "Performance of the JET pumped divertor cryopump system," Proceedings of 16th International Symposium on Fusion Engineering, Champaign, IL, USA, 1995, pp. 742-745 vol.1, doi: 10.1109/FUSION.1995.534329
C.F. Maggi et al 1999 Nucl. Fusion 39 979