## Slide 1: 2D divertor target design based on a priori first principles
Thierry Kremeyer1
1 Max Planck Inst. for Plasma Physics, 17491 Greifswald, Germany
Notes: Thierry Kremeyer, PostDoc at Max Planck Inst für PlasmaPhysik
Work on particle fueling and exhaust
Thank the committee for the oportunity to give this talk, in front of a live audience
Thank all my Co-authors, in particular the Fueling & Exhaust Team, as well as the entire W7-X Team

## Slide 2: Reactor performance requirements
  ΓHe,exhaust = Γα,1
  Minimize Reff for impurities
W7-X
ne = 2 E+20 m-3
Scale with ALCFS
[S. Lazerson PPCF 2021]
[S. Dräger]
[Reiter NF 1990]

## Slide 3: Opertational performance requirements
  Stable density in equilibrium
  Γexhaust = Γsource
  Wall independent density control
  Γexhaust > Γwall
  Γexhaust > 1.1E+21 e/s
  Exhaust limited density control
  Γexhaust < Γwall + ΓNBI + Γpellet (+ΓGas)
  Γexhaust < 1.4E+22 e/s (4.1E+23)
  Fueling limited density control
  Γexhaust > Γwall + ΓNBI + Γpellet (+ΓGas)

## Slide 4: Guarantee requirements
  Survive Pdiv = Prec,surf(Γion,div) + Prec,vol,div(Γion,div) + Prad,div + Pn,div
  qdiv ≤ 10 MW/m² (qmax ≤ 20 MW/m²)
  Survive neutron dpa (ITER 0.14 - 2.5dpa; DEMO 70 – 80 dpa)
  Te,t < 10 eV (< 5 eV W sputtering; < 1.5 eV volume recomb.)
  Objective: Optimize performance metrics
  Maximize Γexhaust combined with throttle
  Minimize Reff

## Slide 5: Particle exhaust metrics and efficiencies
Exhaust efficiencies
Particle collection Particle removal
ηcollection = Γpumpgap / Γneutral ηremoval = Γexhaust / Γpumpgap
= 4 % - 10 % = 2 %
Particle plugging Particle exhaust efficiency
ηplugging = Γrecy, div / (Γneutral – Γexhaust) ηexhaust = Γexhaust / Γneutral = ηcollection ηremoval
= 75 % - 97 % = 0.04% - 0.6 %
Core Edge Divertor Sub-divertor
(Burning plasma) (Plasma) (Plasma + Neutrals) (Neutrals)
Unfavorable particles Favorable particles
Γexhaust
Reff*ΓNeutral
Γneutral
Γpumpgap
Γion,edge
Γrecy, div
Γloss, sub-div
Γrecy, edge
pump gap
Γion,core
Γion,div

## Slide 6: A priori first principles
Limiter
Divert – B = 0
    Closed surfaces, meet at x points, rotational transform visualize
    Visualize super x, snowflake, single null, double null,
    3D plot tripple product rho
    Tripple product density temperature confinement
Neutralization Γion,div ΓNeutral
– Only neutral particles can be exhausted
      Surface recombination on target, Prec,surf = Γion,div ((γTe)+(½mionvion²)+εi)
      Volume recombination, preferred, Te,t < 1.5 eV, MAR ~ne,n0, EIR ~ ne³
      for Awetted,max
Minimize Reff for impurities
– Keep recycling particles outside of core
      Ionize outside of LCFS, minimize λiz,He, Te ≥ 100 eV, ~ ne
      Minimize inward impurity transport
      Minimize sputtering source, Te,t < 5 eV
      Reff,H(frad=0.85) = 7 % Reff,H(frad=0.90) = 30 %
      Helium?
MAR
[Stangeby 2000]
[Ralf Schneider]

## Slide 7: A priori first principles
Particle collection ηcollection = 4% - 10%
– Maximize favorable particles
      Direct collection Only if dSL-PG <
      Optimize
      Indirect collection Build up neutral pressure,
      Keep favorable neutrals neutral,
      Optimize
      Continous flow Driven by pressure gradient
Sub-divertor removal ηremoval = 2%
– Decrease Γsub-div loss
– Turn pumpgap into one-way
      Molecular flow Directed reflections, Funnel
      Continuos flow at pumpgap Minimize

## Slide 8: A priori first principles
Plugging ηplugging = 75 % – 97 %
– Block escaping neutrals
– Relevance decreases as ηexhaust increases
      Hardware (Baffles): Thermal loads
      Re-Ionization: Weakend by detachment?
Survive heat loads
– Exhaust heat necessary for particle exhaust
– Radiate rest
    Surface recombination on target
    Volume recombination in front of target
    Radiated power Radiation location and stability:
      X-Point vs homogenous island radiation
      Neutron power

## Slide 9: 2D Target cross section of „standardized“ sections
Targets
Targets
Baffle
Lmin= 2*λiz or 2*
Baffle
Dome/ Double Baffle
Smallest possible angle?
Smallest possible radius?
L
Build up neutral pressure
Optimize
Block escaping neutrals
      Hardware (Baffles) !Thermal loads!
      Re-Ionization
    Direct collection
      Optimize
      CVP ideally normal to target
CVP
Notes: Only one configuration
Moveable baffle / target