## Slide 1: The Wendelstein 7-X stellarator
O. Grulke

## Slide 2: Content The Wendelstein 7-X stellarator and its optimization criteria Operation achievements and transport assessment Operation planning

## Slide 3: Wendelstein 7-X
support structure, supply
plasma shape
50 non-planar superconducting coils
20 planar superconducting coils
outer cryostat vessel
3.4 K

## Slide 4: Wendelstein 7-X – facts and figures
project start 1996
1st large components 2004
12 years of assembly
1.3 mio assembly hours
device final stage 2022
cryogenic 3.4 K device
1000 t total weight
15 m outer diameter
capital investment 400 mio €
total project cost 1.3 bn €

## Slide 5: Wendelstein 7-X – operation parameters
quantity | unit | value
magnetic induction | T | 2.5
rotational transform | 2 | 5/6 … 5/4
ECRH power | MW | 8.5 (>10)
NBI power | MW | 8 (>10)
Neutral gas |  | H2, He (D2)
PFC |  | mostly carbon
max. heating energy | GJ | 18
steady-state divertor heat flux | MW/m2 | 10
typical pulse length (max.) | s | <30 (1800)

## Slide 6: Island divertor concept
magnetic islands
novel divertor concept to allow for a controlled heat and particle exhaust
resonant magnetic islands are intersected by divertor plates

## Slide 7: Island divertor concept
novel divertor concept to allow for a controlled heat and particle exhaust
resonant magnetic islands are intersected by divertor plates
  three-dimensional magnetic field requires three-dimensional divertor geometry

## Slide 8: Island divertor concept
novel divertor concept to allow for a controlled heat and particle exhaust
resonant magnetic islands are intersected by divertor plates
  three-dimensional magnetic field requires three-dimensional divertor geometry
  island geometry is an important operation control parameter

## Slide 9: Optimization criteria and operation goals
coupled 3d-codes to achieve:
MHD equilibrium
MHD stability
neoclassical transport
guiding center drifts
island divertor

## Slide 10: Optimization criteria and operation goals
coupled 3d-codes to achieve:
MHD equilibrium
MHD stability
neoclassical transport
guiding center drifts
island divertor
I | long-pulse operation | 30min discharges @ 18GJ energy turnaround
II. | good finite-b equilibrium and MHD stability | high-b operation (b≥3%)
III. | good neoclassical confinement | at reactor relevant collisionalities
IV. | stiff magnetic field geometry | high-b operation
V. | good collisionless a-particle confinement | high-b operation
VI. | compatible core-edge scenarios | divertor operation w/ control of PFC heat fluxes
VII. | reactor-relevant first wall | future operation with all-metallic PFCs
The mission of Wendelstein 7-X is to demonstrate the physics basis for a HELIAS reactor concept.

## Slide 11: History of operation
operation phase OP 1.1: 2015 / 2016
no divertor
uncovered first wall
technical demonstration
operation phase OP 1.2: 2017 / 2018
uncooled divertor units
full wall coverage
discharge lengths up to 100s
achieved energy throughput 200MJ
operation phase OP 2.1: 2022/2023
fully water-cooled divertor units with cryo pumps
water-cooled first wall
self limitation to 1GJ energy throughput
discharge lengths up to 8min
achieved energy throughput 1.3GJ
to be increased to 30min@18GJ in upcoming campaigns

## Slide 12: First milestone: 1.3GJ energy turnaround

## Slide 13: Long-pulse detachment
  feed-forward Ne seeding to stabilize detachment
   puff of ~8·1017 Ne atoms every 2.5s to keep radiated power constant at frad=0.8
   no influence on density control or core plasma parameters (Zeff=1.5 throughout entire discharge)
  strongly reduced divertor heat flux at Pheat≈1MW/m2
  programmed pulse length of 110s achieved
   stability of scenario allows for much longer pulse lengths (will be addressed in upcoming experimental campaign)
   it is foreseen to introduce feedback on radiative power levels to counteract changes in impurity radiation in long pulse scenarios

## Slide 14: Neoclassical transport
stellarators generally suffer from enhanced neoclassical transport at low plasma collisionality
dependence on magnetic field ripple eff allows for geometrical optimization of the magnetic field to reduce neoclassical diffusion to tokamak level
 a major optimization criterion for the
Wendelstein 7-X stellarator
ion transport affected by ambipolar neoclassical radial electric field
operation at high plasma density is instrumental!
Effect of radial electric field
Delectrons
Helander et al. Plasma Phys. Control. Fusion 54 (2012)
Stellarator optimization
reducing eff

## Slide 15: Wendelstein 7-X configuration

## Slide 16: Wendelstein 7-X configuration
  neoclassical transport optimization due to strongly reduced effective magnetic ripple eeff

## Slide 17
  actual plasma performance demonstrates that neoclassical transport is strongly reduced
  operation scenario dominated by neoclassical transport
  balance heating power against neoclassical power losses
observed performance would not be possible without
strongly reduced neoclassical transport
C.D. Beidler et al., Nature 2021
Experimental demonstration of neoclassical transport optimization

## Slide 18: Dominance of turbulent transport
  impurity transport a good proxy for plasma energy transport
  tracking tracer amounts of injected impurities allow for a detailed quantitative study of turbulent and neoclassical transport
  turbulent transport generally orders of magnitude larger than neoclassical transport
  dependency on temperature ratio aligns with the hypothesis of dominant ITG transport

## Slide 19: Gradient-driven instabilities
ion temperature gradient modes (ITG)
simple fluid instability criterion

## Slide 20: Gradient-driven instabilities
ion temperature gradient modes (ITG)
simple fluid instability criterion
electron temperature gradient modes (ETG)
ETG can contribute considerable to electron heat
transport in tokamaks by the formation of streamers
(small kr)
in stellarators with multiple magnetic field periods,
local magnetic shear prevents streamer formation
 ETG turbulent transport small
G.G. Plunck et al., Phys. Rev. Letters 2019
tokamak
W7-X

## Slide 21: Gradient-driven instabilities
ion temperature gradient modes (ITG)
simple fluid instability criterion
trapped electron modes (TEM)
results from resonance between trapped electron precession
and drift wave phase velocity
 for centrally-peaked density profiles, no resonance for max(J) configurations (J peaks in center)
possibility to stabilize ITG turbulence via density gradient, but not to the expense of TEM destabilization
P. Helander et al., Phys. Plasmas 2013

## Slide 22: Electron heat flux
  ECRH deposition allows for controlled variations of Te (off-axis heating)
  tracking of centrally deposited ECRH heat pulses allows for direct measurements of electron heat transport
  measured electron heat flux does not show indications of strong stiffness
  in agreement with flux-tube simulations of ITG heat transport
G. M. Weir et al., Nucl. Fusion 2021

## Slide 23: Increased heat transport limits Ti operation regime
  observed peak ion temperatures consistently smaller than expected from neoclassical transport
  for available plasma heating powers, Ti≤1.5keV in the ECRH gas-fueled discharges
  often denoted as „ion temperature clamping“
  However…

## Slide 24: Exceptional confinement scenarios
operation scenarios with small turbulent heat flux
confinement approaching the neoclassical transport limit
 operation with centrally peaked plasma density profiles

## Slide 25: Reduced plasma turbulence with NBI fueling
improved confinement phase is observed as long as central density peaking is maintained
critical dependence on ECRH heating level (density pump-out)
loss of density peaking correlates with increase of turbulence

## Slide 26: Not the full story…
little understanding of particle transport

## Slide 27: Not the full story…
little understanding of particle transport
role of ambipolar neoclassical electric field

## Slide 28: Not the full story…
little understanding of particle transport
role of ambipolar neoclassical electric field
I
III
II
saturation of ITG and role of zonal flows

## Slide 29: Not the full story…
little understanding of particle transport
role of ambipolar neoclassical electric field
I
III
II
saturation of ITG and role of zonal flows
turbulence at increased plasma-b and role of KBM

## Slide 30: Figure of merit

## Slide 31: Figure of merit

## Slide 32: Figure of merit

## Slide 33: Operation planning