## Slide 1: Development of long pulse detached scenario at Wendelstein 7-X
M. Jakubowski, M. Krychowiak, et al.

## Slide 2: Main Objectives of TF II in OP2.1 and OP2.2
Main objectives | Scientific goal | Measures of success/Deliverables
Development of long, stationary divertor detachment scenarios with and without impurity seeding | Creating conditions for detachment o Impurity seeding; edge impurity concentration o Edge radiation losses o Optimization of edge topology (control/trim coils) o Dependence on core fueling/heating mechanisms Compatibility with high-performance scenarios o High-mirror and high-iota configurations in comparison with the standard configuration o Pellet-fueled discharges o Exhaust efficiency under detachment | Demonstration of scenarios with long, stationary divertor detachment, in particular, for high-mirror, high-iota and standard configuration Characterize the conditions under which detachment is possible Attain detachment during a high-performance discharge Achieve rapid transition to detachment

## Slide 3: Intrinsic detachment

## Slide 4: Plasma radiation proportional to C2+ intensity and plasma density
Obtaining detachment with help of intrinsic impurities (carbon) is rather straightforward at W7-X.
In order to reach certain level of radiated power we need to increase carbon concentration/radiation at the plasma edge (via plasma density).
V. Perseo et al 2021 Nucl. Fusion 61 116039

## Slide 5: Density required to reach detachment. Limitation at 161019 m-2
V. Perseo et al 2021 Nucl. Fusion 61 116039
Absorption of O2 ECRH becomes inefficient

## Slide 6: Detachment can be obtained by raising the plasma density
Obtaining detachment with help of intrinsic impurities (carbon) is rather straightforward at W7-X.
In order to reach certain level of radiated power we need to increase carbon concentration at the plasma edge (via plasma density).
In a typical W7-X detachment discharge plasma line integrated density is raised to a level above 11020 m-2, which leads to frad > 80%.
This leads to strong reduction of peak heat load > 8 and particle fluxes, i.e. plasma detachment.
This state could be easily maintained with feedback for the whole plasma duration thanks to PID controller.
M. Jakubowski et al 2021 Nucl. Fusion 61 106003
O. Schmitz et al 2021 Nucl. Fusion 61 016026
[M. Krychowiak, et al., NME, 34 (2023) 101363]
proxies for detachment level
Notes: Feedback control system

## Slide 7: Intrinsic detachment could be prolonged in OP2.1 to 100 s
This scenario could be successfully prolonged in OP2, with 100 s long detached discharge
The feedback system was controlling plasma density and not plasma radiation.
Radiation fraction of ca. 80% required higher plasma density than in OP1.2
No significant increase of core impurities
Feedback control:
  On Prad (constant PECRH necessary)
  Otherwise on frad
not stable on longer time scales
Notes: Feedback control system

## Slide 8: Intrinsic detachment could be prolonged in OP2.1 to 100 s
Notes: Feedback control system

## Slide 9: Lower carbon contents at the plasma boundary due to boronizations
Boronization produces amorphous boron containing carbon films a-C/B:H on a plasma surface, which has a strong ability to gatter oxygen.
  In OP1.2: Oxygen reduced by a factor of 10 (or a lot more, in some cases)
  Carbon reduced by about a factor of 7, to large degree due to much lower oxygen content at the plasma edge.
After 1 boronization
Boronization effects in OP1.2
T. Wauters, et al., Nucl. Mat. Ene. 17 (2018) 235–2
Notes: Feedback control system

## Slide 10: Lower carbon contents at the plasma boundary due to boronizations
Boronization effects in OP1.2
T. Wauters, et al., Nucl. Mat. Ene. 17 (2018) 235–2
Inefficient absorption O2 ECRH
After 3 boronizations
Boronization produces amorphous boron containing carbon films a-C/B:H on a plasma surface, which has a strong ability to gatter oxygen.
  In OP1.2: Oxygen reduced by a factor of 10 (or a lot more, in some cases)
  Carbon reduced by about a factor of 7, to large degree due to much lower oxygen content at the plasma edge.
Notes: Feedback control system

## Slide 11: Seeded detachment

## Slide 12: Set-up of seeding detachment experiments
Injecting Ne or N2 through a one out of ten divertor injection systems into an island SOL.
Krychowiak, M., et al., Rev. Sci. Instrum. 87 (2016) 11D304
F. Effenberg et al 2019 Nucl. Fusion 59 106020
Injection of Ne
Injection of N2

## Slide 13: Choice of seeding impurities for heat load control
The choice of impurities or the mix of several impurities will depend on the expected temperature range, the achievable impurity density nZ and ne.
As the SOL at W7-X is supposed to operate at plasma electron temperatures of few to 10 eV the choice of impurities is limited to low- or medium-Z species, e.g. N2 or Ne.
Especially nitrogen seems to be attractive impurity as it LZ characteristics is similar to carbon
SOL of island divertor at Wendelstein 7-X
Lz calculated for coronal equilibrium [1]
[1] M. Wischmeier, et al., IAEA-FEC TH/P7-5 (2018)

## Slide 14: Detachment with neon seeding long living due to high recycling of Ne
C
C
C + Ne
C + Ne
C + remaining Ne
C + remaining Ne
Prad  1.5 MW

## Slide 15: Due to very efficient boronization low carbon contents, detachment aided by impurities seeding.
Due to very efficient boronization low carbon concentration at the plasma edge.
Detachment (frad > 70%) had to be aided with seeded impurities (Ne, N2)
This needed careful scenario development (no feedback on plasma radiation yet).
Scenario development allowed to reach frad > 80% required for steady-state.
seeded with too little Ne
seeded with enough Ne

## Slide 16: Longest detached scenario with Ne seeding
After several attempts (no feedback on frad possible before OP2.3), an optimized scenario has been found, which allowed to reach proper PSOL/Prad to keep both vulnerable components in the safe temperature range and aim at 1 GJ.
Puff of ca. 8·1017 Ne atoms every 2.5 seconds kept Prad baseline constant at frad = 0.8 in the first 18 seconds. Gyrotrons dropped after t = 18 s

## Slide 17: Longest detachment program in OP2.1 (seeding Ne)
After several attempts (no feedback on frad possible before OP2.3), an optimized scenario has been found, which allowed to reach proper PSOL/Prad to keep both vulnerable components in the safe temperature range and aim at 1 GJ.
Puff of Ne every 2.5 seconds kept Prad baseline constant at frad = 0.8 in the first 18 seconds. Gyrotrons dropped after t = 18 s

## Slide 18: High mirror and high-iota configuration
Only a handful of discharges with intrinsic detachment performed (plus one in reversed field).
Operational window not scanned
No seeded detachment proposals performed
AEI pressure guages not available
The results are very promissing and require more thorough investigastion in OP2.2/2.3
High iota programs were not executed in OP2.1
High mirror, forward Btor
subdivertor pressure remains at the pre-detachment level, no roll over?
M. Jakubowski | W7X Workshop 2023

## Slide 19: Feedback control needs for long pulse detachment
OP1.2b
  Prad control used to develop stable detachment scenarios
  ne control sufficient for ~30 sec. programs
OP2.1
  Prad control not available
  Scenario development (~100 sec.) with just ne control time consuming
What we need
  Either: Prad control + stable ECRH power
  Or: frad control
  Or: Other proxies for detachment level
    CII/CIII radiation in the edge filterscopes (detachment stabilization demonstrated in OP1.2b)
    Neutral gas pressure
    Tsurf
[M. Krychowiak, et al., NME, 34 (2023) 101363]

## Slide 20: Summary
Both intrinsic and seeded detachment experiments were performed in standard configuration.
Inefficient development of seeded detachment scenarios without feedback on Prad (and sometimes even without Prad)
Boronization reduces frad level for a given plasma density such that detachment for PECRH > 4 MW not possible without additional Ne or N2.
We were able to extend the duration of the pulse from 30 s to >100 s for intrinsic and seeded detachment, but we could not optimize the performance (frad > 95%) for most of the pulse.
It will be difficult to extend the seeded detachment beyond 100 s without proper feedback system.
High mirror and high iota are very promising for detachment and higher plasma performance, yet almost no experiments were performed in OP2.1.