## Slide 1: Overview: particle exhaust and gas balance
V. Haak, T. Bräuer, CP. Dhard, T. Kremeyer, G. Motojima, D. Naujoks, G. Schlisio, H. Viebke, O. Volzke, W7-X Team

## Slide 2: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Method: determine decay of line integrated density after gas puffs
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 3: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Decay Experiment: | Gas puff
Standard – EJM | With CVP: 11.00 s ± 0.86 s Without CVP: 10.99 s ± 1.82 s
High Iota – FTM | With CVP: 6.63 s ± 1.00 s Without CVP: no data
High Mirror – KKM | With CVP: 5.56 s ± 1.03 s Without CVP: no data
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 4: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Method: determine decay of line integrated density when switching gas inlet on and off
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 5: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Decay Experiment: | Gas puff | Gas inlet on/off
Standard – EJM | With CVP: 11.00 s ± 0.86 s Without CVP: 10.99 s ± 1.82 s | With CVP: no data Without CVP: 11.30 s ± 1.07 s
High Iota – FTM | With CVP: 6.63 s ± 1.00 s Without CVP: no data | With CVP: 7.59 s ± 0.29 s Without CVP: no data
High Mirror – KKM | With CVP: 5.56 s ± 1.03 s Without CVP: no data | With CVP: 4.99 s ± 1.06 s Without CVP: no data
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 6: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Method: determine decay of line integrated density after switching gas inlet off
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 7: Effective particle confinement time for hydrogen (Thierry Kremeyer)
Different confinement times during density decay observed
Confinement times determined using this method much higher than for the other methods
Why does τH* peak?
KKM without CVP
EJM without CVP
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 8: Effective particle confinement time for hydrogen (Thierry Kremeyer)
The effective confinement time τp* describes how long a particle spends in the machine before being exhausted. It is therefore a key metric for particle exhaust (besides Seff, pn, Γexhaust)
It is measured by fitting an exponential decay to the density signal at ne = 6 E+19 m-2
τp* strongly wall dependent, as the wall can act as additional source or sink
Decay Experiment: | Gas puff | Gas inlet on/off | Gas inlett off
Standard – EJM | With CVP: 11.00 s ± 0.86 s Without CVP: 10.99 s ± 1.82 s | With CVP: no data Without CVP: 11.30 s ± 1.07 s | 
High Iota – FTM | With CVP: 6.63 s ± 1.00 s Without CVP: no data | With CVP: 7.59 s ± 0.29 s Without CVP: no data | 
High Mirror – KKM | With CVP: 5.56 s ± 1.03 s Without CVP: no data | With CVP: 4.99 s ± 1.06 s Without CVP: no data | 
EJM without CVP
KKM without CVP
Notes: When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*
When talking about particle exhaust, the key metric is the exhaust rate, how many particles/s we exhaust – Γexhaust. Which is calculated by multiplying the effective pumping speed Seff with the neutral gas presser pn. Experiments for these metrics completed last week.
Another key metric is the effective particle confinement time, τH*, which describes how long a particle effectively spends in the machine, before being exhausted.
Measured through fitting an exponential decay to density signal. 3 different Experimental set ups:
Gas puff – additionaly to τH* fueling efficiency 𝜂_(𝑐𝑜𝑟𝑒 𝑓𝑢𝑒𝑙𝑖𝑛𝑔) of fueling system used and S/XBeff - effective photon/particle conversion factors.
*CLICK*
Feedback on/off – only τH* but better control over starting density, better statistics and therefore lower uncertainty. Also the traditional way to measure τH*
*CLICK*
Feedback off – gives a density dependance of τH*

## Slide 9: Effective particle confinement time for hydrogen (Gen Motojima)
Effective particle confinement time evaluated from density decay after gas puffs in standard configuration with (Session 9, 07.12.2022) and without CVP (Session 17, 09.02.2023)
Effective confinement time appears shorter with CVP on
Evaluated density window is very narrow, especially without CVP. Further data sets are needed to see the density dependence
Differences in τp* are observed for the same density without CVP, the causes of which need to be investigated in detail for each shot
Effective confinement times overestimated due to contribution of the wall
For = 10s and = 200ms, R = 0.98

## Slide 10: Gas balance with water-cooled divertor (Georg Schlisio)
• 480s plasma duration
• Water-cooled divertor
• Near-constant fueling-density-ratio
• Stable density
20181017.19

## Slide 11: Gas balance with water-cooled divertor (Georg Schlisio)
20230215.32

## Slide 12: Calibration of the neutral gas diagnostics – overview (G. Schlisio)
System | Quantities | Status
Plasma vessel | Volume | Successful
Main gas valves (DCH) | Flow rate as function of valve voltage | Successful
Divertor gas inlet (QSQ) | Flow rate | Under evaluation  A. Tsikouras
NBI | Box volume, getter pump speed | Successful
Neutral gas manometers (QRG) | Total pressure calibration | Successful
WISP-gauges (QRF) | Total and partial pressure cal. | Partially successful
TMPs (ADB) | Pumping speed | It‘s complicated
CVPs | Pumping speed | Under evaluation  V. Haak
ICRH valve characterization | Flow rate | Postponed to OP2.2
GPI valve characterization | Flow rate | Successful
IR endoscope flushing rate | H2 flow rate | Successful

## Slide 13: Neutral gas pressures with and without CVP
Standard configuration
Chart: neutral gas pressure OP1.2b
| 2 | 3 | 3 | 3 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 3.5 | 4 | 4 | 4.5 | 5 | 5 | 6 | 6 | 6 | 6 | 6 | 7 | 7 | 7 | 7 | 7.5 | 7.5 | 7.5 | 8 | 8 | 8 | 8 | 8 | 8 | 9
p_AEH | 1.3031e-05 | 2.6285e-05 | 7.6015e-05 | 7.3514e-05 | 3.235e-05 | 4.3458e-05 | 4.7857e-05 | 4.64e-05 | 4.5898e-05 | 4.8744e-05 | 4.7675e-05 | 4.6968e-05 | 9.2081e-05 | 6.1826e-05 | 0.0001025 | 9.6797e-05 | 8.5724e-05 | 0.000136 | 0.00013481 | 0.00010234 | 6.9908e-05 | 0.00011469 | 0.00014071 | 6.6702e-05 | 0.00019602 | 0.0001613 | 0.00027825 | 0.00019041 | 0.00017593 | 0.00019923 | 0.00020272 | 0.000198 | 0.00014391 | 0.00024332 | 0.00019638 | 0.00032646
p_AEI | 3.0224e-05 | 6.1407e-05 | 0.00014614 | 0.00014334 | 6.5268e-05 | 8.3374e-05 | 8.9706e-05 | 9.4541e-05 | 9.1617e-05 | 8.9019e-05 | 9.0084e-05 | 8.9488e-05 | 0.00017873 | 0.00012402 | 0.00021263 | 0.00016089 | 0.00014593 | 0.00026204 | 0.00023149 | 0.00020019 | 0.00011145 | 0.00018704 | 0.00022088 | 0.00010867 | 0.00035566 | 0.00024438 | 0.00028038 | 0.00029375 | 0.00028523 | 0.0003011 | 0.00030627 | 0.00030841 | 0.00027609 | 0.00042045 | 0.00030483 | 0.00032681
p_AEP | 1.9999e-05 | 2.4591e-05 | 3.4447e-05 | 3.4152e-05 | 3.8189e-05 | 2.4673e-05 | 3.5588e-05 | 3.2484e-05 | 4.7832e-05 | 2.8781e-05 | 4.6567e-05 | 4.8721e-05 | 4.1089e-05 | 3.1566e-05 | 5.5519e-05 | 6.3423e-05 | 7.3702e-05 | 8.2222e-05 | 6.6818e-05 | 6.2002e-05 | 5.5332e-05 | 9.487e-05 | 0.00010983 | 5.3796e-05 | 9.4398e-05 | 0.00011348 | 9.4198e-05 | 0.00011187 | 0.00010712 | 0.00013152 | 0.00014126 | 0.0001276 | 8.8238e-05 | 0.00010883 | 0.0001249 | 0.00011467
p_AEE | 4.2013e-06 | 9.5609e-06 | 2.4248e-06 | 2.3358e-06 | 7.4377e-07 | 7.2917e-07 | 2.0636e-06 | 2.0792e-06 | 2.0998e-06 | 2.1796e-06 | 2.4865e-06 | 2.3926e-06 | 3.3857e-06 | 2.0331e-06 | 1.7333e-06 | 4.2803e-06 | 5.1892e-06 | 2.2998e-06 | 4.4815e-06 | 1.9553e-06 | 1.8457e-06 | 6.5778e-06 | 7.4805e-06 | 2.0385e-06 | 3.648e-06 | 6.9849e-06 | 4.6976e-06 | 9.4632e-06 | 8.9848e-06 | 8.6118e-06 | 9.2363e-06 | 8.0501e-06 | 3.1636e-06 | 7.8199e-06 | 7.5499e-06 | 6.1982e-06
Neutral gas pressures in the same range as during OP1.2b
1e-04 mbar – 5e-04 mbar at pumping gap
4e-05 mbar – 3e-04 mbar at AEH pumping port in subdivertor volume
Slightly lower neutral gas pressures in subdivertor during operation of CVP
Overall no significant impact of CVP on neutral gas pressures in current pressure regime

## Slide 14: Neutral gas pressures with and without CVP
High iota configuration
Neutral gas pressures in the same range as during OP1.2b
1e-04 mbar – 2.5e-04 mbar at pumping gap
4e-05 mbar – 5e-04 mbar at AEP pumping port in subdivertor volume
No comparison between discharges with and without CVP possible
Chart: neutral gas pressure OP1.2b
| 3.5 | 4 | 4 | 5 | 5 | 5 | 5 | 6 | 8 | 15 | 16
p_AEH | 1.0867e-05 | 2.6111e-05 | 1.9602e-05 | 2.2867e-05 | 1.7803e-05 | 2.4256e-05 | 2.7e-05 | 2.1392e-05 | 3.9983e-05 | 7.4908e-05 | 7.5366e-05
p_AEI | 1.3058e-05 | 3.524e-05 | 2.893e-05 | 3.332e-05 | 2.3008e-05 | 3.5215e-05 | 3.8025e-05 | 3.18e-05 | 5.4242e-05 | 9.4306e-05 | 9.3466e-05
p_AEP | 0.0001956 | 0.00042046 | 0.00034245 | 0.00039283 | 0.00029941 | 0.00041206 | 0.00045876 | 0.00030793 | 0.00064556 | 0.001 | 0.00097187
p_AEE | 8.0823e-06 | 4.9625e-06 | 4.4543e-06 | 6.0118e-06 | 2.4027e-06 | 4.7329e-06 | 5.0004e-06 | 6.1004e-06 | 8.1149e-06 | 1.7546e-05 | 1.8396e-05

## Slide 15: Pumping speed of the Cryo-vacuum pump (V. Haak, CP Dhard)
Pumping speed of the cryopump can be determined using the following equations
with pressure measurements in the divertor, the pumping speed can be determined using the steady-state case of the equations during the gas puff (constant pressure)
0
0

## Slide 16: Pumping speed of the Cryo-vacuum pump (V. Haak, CP Dhard)
H2 (15mbar l/s & 20mbar l/s)
CVP Pumping speed of 70.97 m3/s and 70.93 m3/s calculated from H2- gas injection
Good agreement between experiments and time-dependent simulation of the neutral gas pressure in the subdivertor during gas injection
Gas on
Gas off

## Slide 17: Pumping speed of the Cryo-vacuum pump in different gases
More experiments to determine the pumping speed have been performed with (green background) and without (white background) the turbomolecular pumps and with different gases (H2, N2, Ne, Ar, He)
gas | S without TMP (m3/s)
H2 | 71,0 / 71,0
N2 | 21,9 / 19,9
Ne | 22,2 / 21,6
Ar | 9,4 / 9,4

## Slide 18: Summary and planned activities
KKM without CVP
EJM without CVP
Particle confinement times for hydrogen ~11s with and without CVP in standard configuration, likely overestimated due to wall
No data for discharges without CVP in high iota and high mirror configuration
Study of He-confinement times using He-NBI during the next campaign
Determination of τp* based on density decay when gas inlet is switched off
results in much higher confinement times
Preliminary gas balance indicates no significant built-up of wall inventory
with water-cooled divertor
Calibration of divertor gas inlet, ICRH valve and TMPs missing for final gas balance

## Slide 19: Summary and planned activities
No changes in neutral gas pressure in subdivertor despite modifications to subdivertor structures
No significant impact on CVP on neutral gas pressure in the subdivertor in current pressure regime of 4e-05-3e-04mbar in low iota subdivertor volume
No comparison of neutral gas pressure with and without CVP in FTM
How can neutral gas pressure be increased for effective use of the CVP?
Pumping speed of CVP: 71 m3/s for H2
21 m3/s for N2
22 m3/s for Ne
9 m3/s for Ar
Combined pumping speed of CVP and TMPs not easy to determine
Development of numerical conductance models using ANSYS and DIVGAS