## Slide 1: Island structure and turbulence in the scrape-off layer of Wendelstein 7-X: results from OP2.1
Sean Ballinger (sballin@mit.edu) on behalf of the W7-X team
Sean Ballinger | W7-X op2.1 results workshop 28.11.2023 | event.ipp-hgw.mpg.de/event/969/contributions/1509

## Slide 2: Part 1: 3D profiles vs magnetic island details Part 2: attempt at mapping GPI and MPM data Part 3: SOL currents and modes/turbulence

## Slide 3: Good agreement between ICRH density profile reflectometer and Alkali Beam Emission Spectroscopy (ABES)
H.M. Xiang et al., Nuclear Science and Techniques (submitted), 2023

## Slide 4: GPI and MPM provide complementary measurements of turbulence in the outboard island region of W7X
MPM
sampling area
Standard magnetic configuration
GPI with camera rotated 90º
GPI nozzles
GPI normal view

## Slide 5: MPM finds that the island potential structure is aligned with flux surfaces
MMG000+2520
Icc=+1500A
Triple probe profiles
island separatrix
poloidal structure:
higher Vfl and Te for upper pins (towards X point)
positive Vfl around island O point
Vfl structure follows flux surface (outer island separatrix) rather than connection length transition!

## Slide 6: MPM: magnetic structure still important in far SOL of a small plasma
small / detached plasma with almost no SOL density left
still, a small but clearly localized Isat current is measured at the Lc transition

## Slide 7: Poloidal motion is seen to dominate in GPI videos
Original video
Background-subtracted
Standard magnetic configuration
LCFS

## Slide 8: GPI finds consistent poloidal flow pattern near O-point and trend with toroidal current
Island O-point
Edge of closed field line region
Edge of closed field line region
Standard configuration
EJM007+2520 (340 puffs)
zig-zagging of blue/red boundary due to detector resolution
LCFS
LCFS

## Slide 9: MPM confirms GPI observation of high poloidal velocities at high toroidal current
size increases with Ip
closed field lines around island O point
MPM confirms particularly high vpol (~8km/s) for high Ip (10kA)
Size of MPM-measured potential structure and island confined region increase with Ip

## Slide 10: GPI-observed poloidal velocities are due to ErxB drift: when toroidal field is reversed, poloidal velocities reverse
Edge of closed field line region
Edge of closed field line region
Island O-point
Standard configuration
EJM001+2520 (57 puffs)
Standard configuration, reversed field
EJM016-2520 (40 puffs)

## Slide 11: GPI: island size change experiments in standard configuration (reversed field) may indicate that flow directions depend on island O-point location
Note Icc on y-axis instead of Itor; Itor 0 in cases analyzed
Region of negative velocities roughly follows the island O-point
Could be helpful to repeat with more intermediate Icc values
Island O-point
XP_20230118.* (S23, S24)
Icc = 1.5 kA
Icc = 0 kA
Icc = -1.5 kA

## Slide 12: ExB velocities estimated from MPM potential are roughly consistent with GPI velocities
Er structure implies sheared poloidal flows
vpol ~ few km/s (B=2.3T)
Epol implies (small) inwards radial flow, ≈100m/s
flow
flow

## Slide 13: Radial velocities extracted from GPI are in the same ballpark as those found by MPM
Epol implies (small) inwards radial flow, ≈100m/s
flow
Difficult to see radial motion in videos as faster poloidal motion dominates
Difficult to measure radial velocity with standard methods, so using new 3-point time-delay estimation method
MPM Epol (different shot)
GPI velocity field
GPI average velocity in each column
A.D. Helgeland, J.M. Losada, O.E. Garcia

## Slide 14: Part 1: 3D profiles vs magnetic island details Part 2: attempt at mapping GPI and MPM data Part 3: SOL currents and modes/turbulence

## Slide 15: GPI and MPM poloidal velocity patterns can match qualitatively
red = upwards
blue = downwards
gas puff imaging: direct imaging of poloidal flows via spatio-temporal dynamics of fluctuations
probes:
with Er derived from potential distribution

## Slide 16: MPM-GPI comparison in standard config island rotation scan was not fully satisfying
unclear results!
pattern of shear layers sometimes, but not consistently agrees
better FoV overlap of diagnostics would help
possible effect of error fields / toroidal asymmetries (MPM and GPI are in different islands, mapping assumes stellarator symmetry)
would benefit from finer steps in Icc

## Slide 17: GPI: island rotation had little impact on observations in low iota
Icc = 0 A
Icc = +/- 2.5 kA
XP_20230126.54
XP_20230131.9
GPI view is approximate
Icc = -/+ 2.5 kA
XP_20230131.13

## Slide 18: Part 1: 3D profiles vs magnetic island details Part 2: attempt at mapping GPI and MPM data Part 3: SOL currents and modes/turbulence

## Slide 19: MPM: currents in the SOL can cause significant changes to the island flux surfaces
current density of 10kA/m2 !
Directed Electron Probe (DEP) on MPM measures parallel electron currents
First-time operation in OP2.1 shows substantial currents in magnetic islands

## Slide 20: MPM: currents in the SOL can cause significant changes to the island flux surfaces
Directed Electron Probe (DEP) on MPM measures parallel electron currents
First-time operation in OP2.1 shows substantial currents in magnetic islands

## Slide 21: MPM finds different turbulence characteristics in island/center/shadowed regions
technical problems prevent full turbulence analysis (signals only reliable up to 30-50kHz)
high coherence across multiple probe pins inside magnetic islands, low coherence outside
island SOL
target shadow region
island potential structure shows intermittent / quasi-periodic bursts, localized to the island center

## Slide 22: GPI: broadband turbulence with higher kurtosis and skewness is observed in the the target shadow region (230323039)
Two outermost columns are in the region with short connection length
Normal (Gaussian) distributions in the long connection length region, consistent with the past A-BES and MPM measurements

## Slide 23: GPI resolves the radial localization of the quasi-coherent mode (QCM)
QCM [Zoletnik, PPCF (2019)] is localized between the LCFS and the O-point.

## Slide 24: GPI: QCM excitation appears to be sensitive to the poloidal location of the O-point

## Slide 25: GPI and PCI: bursty fluctuation regime exists at low power
Dropouts (< 25% amplitude) and spikes (<70%) on ms timescale observed by PCI (line-integrated through core + SOL) in limited heating power range
Events are quasi-periodic with f ~ 50-200Hz, some density and power dependence
Observed at all densities (and radiation fractions) and in all magnetic configurations
3.6MW
2.8MW
4.5MW
2.0MW
1.3MW
dropouts
spikes
clean

## Slide 26: GPI and PCI: bursty fluctuation regime exists at low power
GPI shows corresponding SOL emissivity changes ~ f(ne,Te) and increase/decrease in turbulent fluctuations
Spikes: ~2ms brightness increase, radial propagation
Dropouts: ~10ms brightness loss, largest in confined O-point and far SOL
Events synchronized with ECE and PCI diagnostics
ECE gradient flattening around inversion radius (ρ≈0.8)
single pixel col. 4

## Slide 27: GPI: SOL fluctuations change during seeded detachment
Core density fluctuations measured by PCI unaffected during seeded detachment
GPI field-of-view: H𝛼 line emission front moves inward and decreases due to local Te (and ne) drop
Normalized δI/<I> profiles follow inward shift, LF and HF components at different radii
Poloidal phase velocities (not shown) decreased, generally vr ≪ vpol
Skewness + kurtosis strongly reduced in detachment, generally poloidally highly asymmetric
fluctuation skewness + kurtosis
SOL (GPI) average/fluctuating H𝛼 brightness profiles
average brightness
standard deviation
LF fluctuation level
HF fluctuation level
FOV bottom
FOV top
FOV bottom
FOV top
HM conf.
HM conf.
HM conf.
Sean Ballinger | W7-X op2.1 results workshop 28.11.2023 | event.ipp-hgw.mpg.de/event/969/contributions/1509

## Slide 28: Summary
ICRH reflectometer and ABES find close agreement in edge density profiles
Profiles and turbulence in island are aligned with flux surfaces but can also depend on connection length profile
GPI and MPM velocity measurements agree qualitatively
  GPI-MPM spatial comparison would benefit from a finer island rotation scan
GPI sees different radial extents of SOL depending on Itor and mirror ratio: modifications to make them more comparable?
Bursty fluctuation regimes could be investigated through further scans
For OP2.2/3 proposal collaboration, contact sballin@mit.edu (GPI), carsten.killer@ipp.mpg.de (MPM)

## Slide 29: GPI: a change in the turbulence statistics of the island divertor SOL is observed between the attached and detached states
Attached:
Detached:
SOL transport is likely to be a spatially dependent process, as seen from the radial and poloidal variations of the moments.